National Hydrography Data Content Standard for Coastal and Inland Waterways – Public Review Draft

Bathymetric Subcommittee

Federal Geographic Data Committee

January 2000

Federal Geographic Data Committee

Established by Office of Management and Budget Circular A-16, the Federal Geographic Data Committee (FGDC) promotes the coordinated development, use, sharing, and dissemination of geographic data.

The FGDC is composed of representatives from the Departments of Agriculture, Commerce, Defense, Energy, Housing and Urban Development, the Interior, State, and Transportation; the Environmental Protection Agency; the Federal Emergency Management Agency; the Library of Congress; the National Aeronautics and Space Administration; the National Archives and Records Administration; and the Tennessee Valley Authority.  Additional Federal agencies participate on FGDC subcommittees and working groups.  The Department of the Interior chairs the committee.

FGDC subcommittees work on issues related to data categories coordinated under the circular.  Subcommittees establish and implement standards for data content, quality, and transfer; encourage the exchange of information and the transfer of data; and organize the collection of geographic data to reduce duplication of effort.  Working groups are established for issues that transcend data categories.

For more information about the committee, or to be added to the committee's newsletter mailing list, please contact:

Federal Geographic Data Committee Secretariat

c/o U.S. Geological Survey

590 National Center

Reston, Virginia 22092

Telephone:  (703) 648-5514

Facsimile:  (703) 648-5755

Internet (electronic mail):  gdc@usgs.gov

Anonymous FTP:  ftp://fgdc.er.usgs.gov/pub/gdc/

World Wide Web:  http://fgdc.er.usgs.gov/fgdc.html

CONTENTS

1.0	INTRODUCTION	1

1.1	OBJECTIVE	1

1.2 	SCOPE	1

1.3	APPLICABILITY	1

1.4	JUSTIFICATION/BENEFITS	2

1.5	RELATED STANDARDS	2

1.6	STANDARDS DEVELOPMENT PROCESS	3

1.7	TARGET AUTHORIZATION BODY	4

1.8	MAINTENANCE AUTHORITY	4

1.9 	PARTS OF THE STANDARD	5

2.0	DEFINITIONS	6

3.0	LOGICAL DATA MODEL	7

4.0	HYDROGRAPHY STANDARD DATA DICTIONARY/OBJECT CATALOG	9

5.0    HYDROGRAPHY STANDARD ATTRIBUTE DEFINITIONS	30

6.0	IMPLEMENTATION	35

7.0	references	37

APPENDIX A  STANDARD CORRELATION OF IHO S-57 (INFORMATIVE)  	38

APPENDIX A1 - Feature Cross Reference     (INFORMATIVE) 	38

APPENDIX A2 - Attribute Cross Reference (INFORMATIVE) 	44

APPENDIX B  STANDARD CORRELATION OF FACC (INFORMATIVE)	81

APPENDIX B1 - Feature Cross Reference (INFORMATIVE) 	81

APPENDIX B2 - Attribute Cross Reference (INFORMATIVE) 	88

APPENDIX C  STANDARD CORRELATION OF REEGIS (INFORMATIVE)	103

APPENDIX C1 - Feature Cross Reference (INFORMATIVE) 	103

APPENDIX C2 - Attribute Cross Reference (INFORMATIVE) 	108

APPENDIX D STANDARD CORRELATION OF TSSDS (INFORMATIVE)	 114

APPENDIX D1 - Feature Cross Reference (INFORMATIVE) 	114

APPENDIX D2 - Attribute Cross Reference (INFORMATIVE) 	120

1.       INTRODUCTION

1.1	OBJECTIVE

Geospatial hydrography data for waterways, shorelines, coastlines, etc. that supports transportation applications has been specified as one of the key framework information layers for the National Spatial Data Infrastructure (NSDI).  The objective of this NSDI Hydrography Data Content Standard for Coastal and Inland Waterways (hereafter called the Hydrography Standard) project is to develop a nationally focused hydrographic data content standard for spatial data that supports safety of navigation.  When complete, this standard will provide a consistent catalog of terms and definitions (semantics) to ensure uniform interpretation of information across a variety of organizations that develop and use hydrographic feature data and applications.  This standard is based upon a well known logical data model for geospatial data of features, attributes, and domain values that is consistent with the Spatial Data Transfer Standard/Federal Information Processing Standard (SDTS/FIPS 173 part 2).

1.2	SCOPE

The scope of this Hydrography Standard project first focused on developing a catalog of hydrographic feature terms and definitions pertaining to navigation of coastal and inland waterways.  In that the guidance from the NSDI concentrated on transportation/navigation, the team limited the scope to information relating to charting and electronic chart display applications.  This standard will not address data distribution formats, extraction criteria, or accuracy reporting methods beyond inland and coastal waterways.  This standard does not currently address hydrographic symbology.  However, in future versions/releases of this standard it is planned to add this standard symbology information.

  - APPLICABILITY

This Hydrography Standard is applicable to any U.S. organization that generates hydrographic feature information that supports coastal and inland waterways navigation.  This standard is also applicable to any U.S. organization that uses hydrographic feature information generated by another organization and must translate its feature schema to a common feature schema based upon a standard hydrographic dictionary.

1.4	JUSTIFICATION/BENEFITS

There has never been a national data content standard for hydrographic data that support navigation applications; yet there has been interest from federal agencies, private industry, and the public for a uniform presentation of this type information for some time.  A data content standard that supports navigation applications will ensure effective use and exchange of geospatial data across multiple agencies, organizations, and other users.

Specifically, this Hydrography Standard will facilitate semantic consistency when capturing geospatial hydrographic information for military and commercial navigation and electronic charting databases (in a GIS or CADD) and provide consistent data for applications that query, analyze this information, and interpreted this information for display of electronic charts.  This standard will support cost savings associated with reducing the translating geospatial hydrographic information.  This standard should also reduce the costs of building navigation applications by eliminating the “multi-fuel” requirement of handling many different type of hydrographic feature information.

1.5	RELATED STANDARDS

This Hydrography Standard closely parallels the hydrographic information contained within the following standards:

International Hydrographic Organization's S57 (IHO S-57) Appendix A, Object Catalog for Digital Hydrographic Data.  IHO is an intergovernmental consultative and technical organization working to support the safety of navigation and the protection of the marine environment.

North Atlantic Treaty Organization’s (NATO) Digital Geographic Information Exchange Standard (DIGEST) Part 4, Feature Attribute Coding Catalog (FACC), a comprehensive coding scheme for features, their attributes and attribute.  This allows for joint naval operations between sovereign countries and requires naval personnel to have familiarity amongst traditional S-57 and FACC.

Tri-Service Spatial Data Standard (TSSDS Release 1.8), which is primarily used for civil and military installation mapping and facility management.

U.S. Army Corps of Engineers (USACE) Regional Engineering and Environmental Geographic Information System (REEGIS) project's data dictionary for inland waterways and primarily used by the USACE for engineering, navigation and flood control structures along the Mississippi River.

Also, this Hydrography Standard contains cross-references to the IHO- S57, NATA FACC, and TSSDS standards.

1.6	STANDARDS DEVELOPMENT PROCESS

This standard was developed under the guidance and procedures specified by the Federal Geographic Data Committee (FGDC) under the authority of the Bathymetric Subcommittee.  The FGDC announced the initiation of this Hydrography Standard project in the Federal Register in 1998 and issued a call for any interested party to participate on the project development team.  The project team that developed this standard was composed of experts from the National Oceanographic and Atmospheric Administration (NOAA) and National Imagery and Mapping Agency (NIMA), the U.S. Army Corps of Engineers and the U.S. Coast Guard, several pilot associations, and private industry representatives.  (These agencies and organizations represented users of various existing Hydrography standards.)  In addition to the expertise brought to this project team from the various organizations represented, key documents were used in the development of this standard.   These standards are cited as references in the Related Standards section of this document.

The first step after the formation of a Hydrography Standard project team was to agree upon the scope of this Hydrography Standard.  The project team then reviewed key documents that consisted of adopted standards and systems that had developed and used hydrographic feature data.  The next step for the project team was to develop a master list of candidate features extracted from the related standards documents.

Next, the project team reviewed the master feature list and eliminated those clearly outside of the agreed to scope.  A detailed comparison of feature terms and definitions extracted from the aforementioned standards was conducted.  From this effort, the team was able to derive a standard feature term and definition for each feature.  As a byproduct of this activity, a matrix was developed, which provides a mapping to related terms, or features, contained in each or the source standards.  These matrices are included as appendices.

The project team has extracted all the attributes derived from the aforementioned standards and culled this list of attributes down to a subset of core attributes to include in the Hydrography standard.  The project team created a domain list for each “category” of feature to facilitate the cross reference.  Other attributes have been grouped into logical collections applicable to individual features to ease implementation.  Finally, a draft Hydrography Standard document was generated to include the features, attributes, and domain terms and definitions lists, and additional descriptive documentation as specified by the FGDC directives on creating an NSDI standard.

1.7	TARGET AUTHORIZATION BODY

The Bathymetric Subcommittee originally proposed the development of this Hydrography Standard as an FGDC standard.  The Bathymetric Subcommittee and the Standards Working Group of the FGDC may pursue a joint FGDC and American National Standards Institute (ANSI) adoption of this standard.  To develop this Hydrography Standard through as an ANSI standard will require the development of an ANSI standard proposal and potentially an ANSI public review.  The Bathymetric Subcommittee may consider  (at a later date) promoting parts of this standard (e.g., inland waterways information) that are not currently part of the S-57 standard to International Hydrographic Organization for inclusion in their standard.

1.8	MAINTENANCE AUTHORITY

The National Oceanographic and Atmospheric Administration (NOAA) is the maintenance organization for the Hydrography Standard for the Federal Geographic Data Committee.  All general questions and comments concerning this standard should be addressed to:

Anne Hale Miglarese, Chair,

NOAA Coastal Services Center
2234 South Hobson Ave. 
Charleston, SC 29404-2413
phone 843-740-1238
fax 803-974-6315
amiglarese@csc.noaa.mil

1.9	PARTS OF THE STANDARD

This Hydrography Standard consists of a detailed main body and four appendices.  The main body of the Hydrography Standard defines the purpose of this standard, the process followed during its development, the organization(s) involved in its development and maintenance, the actual Hydrography Standard Data Dictionary (sometimes called the Object Catalog), and its relationship to other standards. Appendices A through D contain matrix cross-references between the respective source data standards and the Hydrography Data Content Standard.  Appendices A through D are informative and therefore not mandatory.

2.0	DEFINITIONS

For the purpose of this Hydrography Data Content Standard, the following definitions apply.

2.1	attribute – a characteristic of an object  (e.g., an attribute of  hydrography surface course = degree of permanence of the surface course)

2.2 	attribute value - a specific quality or quantity assigned to an attribute for a specific feature instance (e.g., electrical cable material = dry).

  - data content standard - provides the semantic definitions for a set of real world spatial phenomena of significance to a community.  Data Content Standards may be organized and presented in a specified logical data model.

2.4	domain - a finite list (or range) of permissible values for a specified attribute.  Included are tables of: units of measure, types, styles, status, names, methods, materials, dispositions, sources, dimensions, data, classes, etc.  (e.g., degree of permanence = dry, intermittent, permanent, etc . . . )

2.5	feature – definition and description of a set (class of real world phenomena) into which similar feature instances are classified (e.g., shoreline and isohaline_zone_area).

2.6 	feature instance - real-world spatial phenomenon about which data is collected, maintained, and disseminated. (e.g., the McMillan Water Reservoir).  Feature instances are the geospatial objects that are graphically delineated in a spatial database.

2.7	geospatial data - data with implicit or explicit reference to a location relative to the surface of the earth.

2.8	hydrography - the science of the physical conditions, boundaries, flow, and related characteristics of earth's waters

2.9  	navigation – to safely move on or through the water in a vessel.

2.10   semantic content –  natural language information (e.g. names of features, attributes, and their phenomena on the earth’s surface)..

3.0	LOGICAL DATA MODEL

Agreement on a common format is not sufficient to ensure that the geospatial information transferred is meaningful to both the sender and the receiver.  In order to share spatial data (and as part of a SDTS data transfer process) a common data model must be defined and used.  In addition, semantic content of a spatial database (i.e., the entities and associated attribute and attribute value information) must be well defined and agreed upon by an application community and specified in either an off-line document (i.e. data content standard) and/or in the metadata for a given database.  Part 2 of the SDTS is a formal attempt to develop a standardized list of entities.  Additionally application communities that want to share geospatial information are developing data content standards modeled after the SDTS data model.

This Hydrography Standard data model (figure 1.) is based upon the SDTS geospatial data model as presented in Parts 1 and 2 of that standard as well as the specifications in ISO/IEC 8613-10:1995.  The logical data model depicts the real world phenomena represented by features that are characterized by attributes that are assigned attribute values.  This Hydrography Standard defines each of the features and their attributes and specifies a domain list for category attributes; e.g. those which further differentiate the individual features.  In addition, this standard incorporates the use of a Feature Code, which identifies the feature in cryptic form for implementation of the standard.  It also incorporates feature representation information that specifies the allowable graphic representations for each of the features.

Hydrography Data Model

Attributes

Feature                                                                                                         Category List Domain

provides info about                                             is assigned

Figure 1

4.0 	HYDROGRAPHY STANDARD DATA DICTIONARY/OBJECT CATALOG

CODE	FEATURE NAME

HS001	ADMINISTRATION_AREA	Land and water under the rights, powers, or authority of various local, state, and national governments.

CATEGORY	COMMON_NAME	COUNTRY	DESCRIPTION	FORMAL_NAME	HORIZ_ACC	RECORD_DATE	SOURCE_DATE

HS002	AIRPORT/AIRFIELD	An area used for landing, take-off, and movement of aircraft, not including associated buildings, runways, and other facilities, either military or civilian.

COMMON_NAME	CONDITION	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS

HS003	ANCHOR_BERTH	A designated area of water where a single vessel, seaplane, etc. may anchor.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RADIUS	RECORD_DATE	SOURCE_DATE

STATUS

HS004	ANCHORAGE_AREA	A designated area in which vessels anchor or may anchor.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	PERMIT	RECORD_DATE	RESTRICTION	SOURCE_DATE	STATUS

HS005	AQUATIC_VEGETATION_AREA	A discrete area where submerged or partially submerged aquatic flora has been identified.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE

HS006	BEACON	A fixed object used for navigation, usually consisting of a single pile or lattice structure, which may or may not actually be in the water.

CARDINAL	COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	LATERAL

PRIMARY_COLOR	RECORD_DATE	SHAPE	SOURCE_DATE	SPECIAL_PURPOSE	STATUS	VERT_ACC	VERT_DATUM

HS007	BERTH	A named or numbered mooring location, normally alongside a pier or wharf.

COMMON_NAME	DATE_END	DATE_START	DEPTH_ACC	DEPTH_DATUM	DESCRIPTION	DESIGNATOR	FORMAL_NAME	QUALITY	RECORD_DATE	SOURCE_DATE	STATUS

HS008	BOAT_LIFT	A mechanical device for lifting vessels between two levels other than a lock.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE

HS009	BOAT_RAMP	A partially submerged hard surfaced area or fixed (not afloat) structure on a shoreline for launching and retrieving vessels or vehicles.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH

PRIMARY_COLOR	RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	VERT_LENGTH	WIDTH

HS010	BOTTOM_CHARACTERISTICS	Designations used on surveys and charts to indicate the consistency, color and classification of the sea floor, as determined by sampling methods.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	MATERIAL	NATURE_BOTTOM	PRIMARY_COLOR	RECORD_DATE	SOURCE_DATE

HS011	BREAKWATER	A stone structure which is designed to reduce the action of waves and currents near the entrance to river and ports.  Sometimes called a breakwater.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH

PRIMARY_COLOR	RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	VERT_LENGTH	WIDTH

HS012	BRIDGE	A supporting structure used by pedestrians, vehicles, rail traffic, and utility services erected over obstacles   such as a river, chasm, mountain, road or railroad.  BRIDGE PIERS may support the structure at various locations along its length, or it may completely span the obstacle.

BRIDGE_TYPE	CLEARANCE	COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	DESIGNATOR	ELEVATION	FORMAL_NAME

HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH	MATERIAL	NUM_SPANS	PRIMARY_COLOR	RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	VERT_CLEARANCE

VERT_DATUM	WIDTH

HS013	BRIDGE_PIER	The support(s) below the span of a bridge in the form of pillar(s) or abutment(s) for the spans of a bridge.  In general, BRIDGE PIERS are only separately coded if they emerge from the surface of the water such that they may be a hazard to navigation.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	PRIMARY_COLOR	RECORD_DATE	SOURCE_DATE

VERT_ACC	VERT_DATUM	VERT_LENGTH	WIDTH

HS014	BRIDGE_TOWER	A tower or pylon extending above the surface of the bridge.  In general, BRIDGE TOWERS are only separately coded if they may be conveniently used as an aide to navigation.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	DESIGNATOR	FORMAL_NAME	HEIGHT	HORIZ_ACC	PRIMARY_COLOR

RECORD_DATE	SOURCE_DATE	VERT_ACC	VERT_DATUM	VERT_LENGTH	WIDTH

HS015	BUILDING	A relatively permanent structure, roofed and usually walled and designed for some particular use.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	DESIGNATOR	ELEVATION	FORMAL_NAME	FUNCTION	HEIGHT	HORIZ_ACC	LENGTH

NO_FLOORS	PRIMARY_COLOR	RECORD_DATE	SHAPE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS016	BUILT-UP_AREA	An area containing a concentration of buildings and the supporting road or rail network.

COMMON_NAME	CONDITION	DESCRIPTION	FACC_CAT	FORMAL_NAME	HEIGHT	MATERIAL	RECORD_DATE	S_57_CAT	SOURCE_DATE	VERT_ACC	VERT_DATUM

WIDTH

HS017	BUOY	A floating object moored to the bottom in a particular place, as an aid to navigation or for other specific purposes.

CHARACTER	COLOR_PATTERN	COMMON_NAME	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FACC_CAT	FORMAL_NAME	HEIGHT	LATERAL	PERIOD

PRIMARY_COLOR	RADAR_REFLECTOR	RECORD_DATE	S_57_CAT	SHAPE	SOURCE_DATE	SPECIAL_PURPOSE	STATUS

TOP_MARK	VERT_ACC

HS018	CANAL	An excavated shallow- or deep draft watercourse designed for navigation, usually artificially cut through land area to bypass rock outcrops and rapids, or through shallow  intracoastal areas where an adequate depth cannot be maintained at low water periods.  Canal edges or borders usually extend above the water surface with visible banks and important ship and bank interaction effects.

COMMON_NAME	CONDITION	DATE_END	DATE_START	DEPTH	DESCRIPTION	FORMAL_NAME	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH	RECORD_DATE	RESTRICTION

S_57_CAT	SOURCE_DATE	STATUS	WATER_VELOCITY	WIDTH

HS019	CARGO_TRANSHIPMENT_AREA	An area designated for the transfer of cargo from one vessel to another.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS	WIDTH

HS020	CAUSEWAY	A raised roadway of solid structure built primarily to provide a route across wet ground or intertidal area.(Alt)A raised area across low or wet ground used for transportation of pedestrians or vehicles.

CLEARANCE	COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	FORMAL_NAME	HEIGHT	LENGTH	RECORD_DATE	SOURCE_DATE	STATUS	WIDTH

HS021	CAUTION_AREA	Generally, an area where the mariner has to be made aware of circumstances influencing the safety of navigation.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	RECORD_DATE	SOURCE_DATE	STATUS	WIDTH

HS022	CHANNEL_RIVER_SYSTEM(SHALLOW)	An inland waterway system used by shallow-draft (15 feet or less) commercial towing and recreational vessels.  Includes open river navigation systems (Mississippi River below St. Louis, Missouri River, Columbia River below Bonneville Dam) and canalized streams with locks and dams (e.g. Ohio River, Mississippi River above St. Louis, MO

COMMON_NAME	DATE_END	DATE_START	DEPTH_ACC	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS	VERT_DATUM

HS023	CHANNEL_MAINTAINED(DEEP_DRAFT)	Type of navigation channel provided for the movement of vessels with drafts of 15 feet or more designed for open-water navigation including seagoing and intracoastal vessels operating in the Great Lakes.  Deep-draft channels are usually marked and designated on the appropriate navigation charts with known/fixed depth and width parameters.  May be formed and maintained totally, or in part, through excavation,

COMMON_NAME	DATE_END	DATE_START	DEPTH_ACC	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS	VERT_DATUM

HS024	CHECKPOINT	An official place to register, declare or check goods and people.

COMMON_NAME	DEPTH

HS025	COAST_GUARD_STATION	Watch keeping station at which a watch is kept either continuously, or at certain times.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS026	CONTIGUOUS_ZONE	A zone contiguous to a coastal State's territorial sea, which may not extend beyond 24 nautical miles from the baselines from which the breadth of the territorial sea is measured. The coastal state may exercise certain control in this zone subject to the provisions of Internationa Law. (IHO Dictionary, S-32, 5th Edition, 993)

COMMON_NAME	COUNTRY	DATE_END	DATE_START	DESCRIPTION	RECORD_DATE	SOURCE_DATE	STATUS

HS027	CONTINENTAL_SHELF_AREA	The seabed and subsoil of the submarine areas that extend beyond its territorial sea throughout the natural prolongation of its land territory to the outer edge of the continental margin.

COMMON_NAME	COUNTRY	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE

HS028	CONTROL_POINT	A permanently monumented survey control point constructed with an original purpose of establishing spatial location in one or more dimensions from a known reference or datum.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	VERT_ACC	VERT_DATUM

HS029	CONVEYOR	A mechanical apparatus for moving bulk material or people from place to place (as by a moving belt or chain of receptacles).

COLOR_PATTERN	COMMON_NAME	CONDITION	DATE_END	DATE_START	DESCRIPTION	DESIGNATOR	FORMAL_NAME	HEIGHT	HORIZ_ACC	LENGTH	PRIMARY_COLOR

RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	VERT_CLEARANCE	VERT_DATUM	WIDTH

HS030	CRANE	A machine for lifting, shifting and lowering objects or materials by means of a swinging boom or with a lifting apparatus supported on an overhead track.

COLOR_PATTERN	COMMON_NAME	CONDITION	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	LENGTH	MATERIAL	PRIMARY_COLOR	RECORD_DATE	SHAPE

SOURCE_DATE	STATUS	VERT_ACC	VERT_CLEARANCE	VERT_DATUM	WIDTH

HS031	CURRENT	Currents (non-gravitational) include either singly or in combination: ocean currents, inter-oceanic equalizing currents, currents of navigable rivers, river outflow effects offshore and other non-tidal flows.

COMMON_NAME	DATE_END	DATE_START	FORMAL_NAME	ORIENTATION	RECORD_DATE	SOURCE_DATE	VELOCITY

HS032	CUSTOM_ZONE	The area within which national customs regulations are in force.

COUNTRY	DESCRIPTION	RECORD_DATE	SOURCE_DATE	STATUS	WIDTH

HS033	DAM	A barrier constructed to hold back water and raise its level to form a reservoir or to prevent flooding.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	LENGTH	PRIMARY_COLOR	RECORD_DATE

SOURCE_DATE	VERT_ACC	VERT_DATUM	WIDTH

HS034	DAY_MARK	The daytime identifier of an aid to navigation.  The daymark conveys to the mariner, during daylight hours, the same significance as does the aid to naviation's light at night.

COLOR_PATTERN	COMMON_NAME	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	PRIMARY_COLOR	RECORD_DATE	S_57_CAT

SHAPE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM

HS035	DEEP_WATER_ROUTE	A deep water route in a designated area, within defined limits, which has been accurately surveyed for clearance of sea bottom and submerged obstacles to a minimum indicated depth of water.

COMMON_NAME	DATE_END	DATE_START	DEPTH_ACC	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS	VERT_DATUM

HS036	DEPTH_AREA	A depth area is a water area whose depth is within a defined range of values.

DESCRIPTION	RECORD_DATE	SOURCE_DATE	VERT_DATUM

HS037	DEPTH_CONTOUR	A line connecting points of equal water depth which is sometimes significantly displaced outside of soundings, symbols and other chart detail for clarity as well as generalization.

DEPTH	DESCRIPTION	RECORD_DATE	SOURCE_DATE	VERT_DATUM

HS038	DISTANCE_MARK	A distance mark indicates the distance measured from an origin and consists of either a solid visible structure or a distinct location without special installation.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	RIVER_MILE	SOURCE_DATE

HS039	DOLPHIN	A post or group of posts, which may suport a deck, used for mooring or warping a vessel.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	PRIMARY_COLOR	RECORD_DATE	SHAPE

SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM

HS040	DREDGED_AREA	An area of the bottom of a body of water which has been deepened by dredging.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	LENGTH	PERMIT	RECORD_DATE	RESTRICTION	SOURCE_DATE	VERT_DATUM

HS041	DRYDOCK	A structure, providing support for a vessel, which has a means of removing water so that the bottom of the vessel can be exposed.

COMMON_NAME	CONDITION	DESCRIPTION	FORMAL_NAME	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH	RECORD_DATE	SOURCE_DATE	STATUS	VERT_DATUM	WIDTH

HS042	DUMPING_GROUND	An area where dredged material or potentially harmful material e.g. explosives chemical waste is deliberately deposited.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	WIDTH

HS043	DYKE	A linear stone structure with a peaked or trapezoidal section located in pointway, secondary and main channel area and typically extending channelward from the 	convex bank to improve channel for navigational and flood control purposes.

COMMON_NAME	DESCRIPTION	ELEVATION	LENGTH	RECORD_DATE	SOURCE_DATE

HS044	ELEVATION	An elevation is the vertical distance of a point or a level, on, or affixed to, the surface of the earth, measured from a specified Geodetic vertical datum.

COMMON_NAME	DESCRIPTION	DESIGNATOR	ELEVATION	FORMAL_NAME	HORIZ_ACC	MATERIAL	RECORD_DATE	SOURCE_DATE	VERT_ACC	VERT_DATUM

HS045	FAIRWAY	A navigable pathway in an open and unobstructed waterway, such as a bay, lake, sound, or straight, or open coast, usually leading into a harbor from the open sea outside a buoyed channel, ordinarily used by vessel traffic, and so designated by appropriate authority.

COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	ELEVATION	FORMAL_NAME			RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS046	FENCE/WALL	A natural or man-made barrier used as an enclosure or boundary or for protection.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE

STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS047	FENDER	A protective structure designed to cushion the impact of a vessel and prevent

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH

PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS048	FERRY_ROUTE	A route in a body of water where a ferry crosses from one shoreline to another.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	TRIP_LENGTH

HS049	FISHERY_ZONE	The offshore zone in which exclusive fishing rights and management are held by the coastal nation.

COMMON_NAME	COUNTRY	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS

HS050	FISHING_FACILITY	A structure in shallow water for fishing purposes which can be an obstruction to ships in general.  The position of these structures may vary frequently over time.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	HEIGHT	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC

HS051	FISHING_GROUND	A water area in which fishing is frequently carried on.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS

HS052	FISHING_HARBOR	A harbour with facilities for fishing boats.

COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS053	FLEETING_AREA	Area where barges and tows are assembled into a fleet.

COMMON_NAME	DESCRIPTION	PERMIT

HS054	FLOATING_DOCK	A facility which can be raised or lowered into the water which can serve as a launching place for vessels or as a floating drydock.

COLOR_PATTERN	COMMON_NAME	CONDITION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH	PRIMARY_COLOR

RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS055	FLOOD_DIVERSION_AREA	An area specifically intended to be covered with water to permit reduction in

river/waterbody water levels protecting more critical areas from inundation.

COMMON_NAME	DESCRIPTION

HS056	FLOODWALL	A structure erected to protect an area from high river stages.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE

LENGTH	PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM

WIDTH

HS057	FOG_SIGNAL	A warning signal transmitted by a vessel, or aid to navigation, during periods of low visibility.  Also, the device producing such a signal.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	FREQUENCY	PERIOD	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS058	FORTIFIED_STRUCTURE	A structure for the military defence of a site.

COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	RECORD_DATE	S_57_CAT	SOURCE_DATE	VERT_ACC	VERT_DATUM

WIDTH

HS059	FOUL_GROUND	An area of numerous unidentified dangers to navigation.  The area serves as a warning to the mariner  that all dangers are not identified individually and that navigation through the area may be hazardous.  Commonly used to encode areas behind danger lines on navigation charts. (adapted from IHO Dictionary, S-32, 5th Edition)

COMMON_NAME	CONDITION	CONSTRUCTION	DEPTH	DESCRIPTION	FORMAL_NAME	HEIGHT	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC

VERT_DATUM

HS060	FREEPORT_AREA	A port where certain import and export duties are waived to facilitate reshipment to other countries.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS	WIDTH

HS061	GATE	A structure that may be swung, drawn, or lowered to block an entrance or

passageway. (United States Geological Survey, Jan.89)

COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	FORMAL_NAME	HORIZ_ACC	HORIZ_CLEARANCE	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC

VERT_CLEARANCE	VERT_DATUM	WIDTH

HS062	GAUGING_STATION	A device which monitors stream flow and water elevation.

COMM_CHANNEL	COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS063	GRAIN_ELEVATOR/ELEVATOR	A tall structure used to store and distribute grain whose location accuracy is not sufficient for naviation purposes.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	PRIMARY_COLOR	RECORD_DATE	S_57_CAT

SHAPE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS064	GRIDIRON	A flat frame, usually of parallel timber baulks, erected on the foreshore so that a vessel may dry out on it for painting or repair at low water.

COMMON_NAME	CONSTRUCTION	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	LENGTH	RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	WIDTH

HS065	GUIDE_WALL	The structure used to guide boats or ships into a lock chamber.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH

PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS066	HARBOR	A natural or artificial improved body of water providing protection for vessels and anchorage and docking facilities.

COMMON_NAME	DEPTH	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS

HS067	HARBOR_FACILITY	A harbor installation with a service or commercial operation of public interest.

COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS068	ICE_AREA	An area which is covered by ice for the entire year.

COMMON_NAME	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS069	ICE_BOOM	Floating barriers, anchored to the bottom, used to deflect the path of floating ice in order to prevent the obstruction of locks, intakes etc., and to prevent damage to bridge piers and other structures.

COMMON_NAME	CONDITION	CONSTRUCTION	DEPTH	DESCRIPTION	FORMAL_NAME	HEIGHT	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC

VERT_DATUM

HS070	INCINERATION_AREA	An offshore area officially designated as suitable for the burning of chemical waste by specially equipped ships.

COMMON_NAME	DEPTH	DESCRIPTION	FORMAL_NAME	RECORD_DATE	RESTRICTION	SOURCE_DATE	STATUS	WIDTH

HS071	INSHORE_TRAFFIC_ZONE	A routeing measure comprising a designated area between the landward boundary of a traffic separation scheme and the adjacent coast, to be used in accordance with the provisions of the International  Regulations for Preventing Collisions at Sea.

COMMON_NAME	DATE_END	DATE_START	DEPTH	DESCRIPTION	FACC_CAT	RECORD_DATE	RESTRICTION	S_57_CAT	SOURCE_DATE	STATUS	WIDTH

HS072	ISLAND	An area of land completely surrounded by the waters of an ocean, sea, lake, or stream.

COMMON_NAME	CONDITION	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	RECORD_DATE	SOURCE_DATE	STATUS	WIDTH

HS073	ISOGONIC_LINE	Lines connecting point of equal magnetic variation.

MAG_VARIATION

HS074	LAKE	Any body of water surrounded by land.

COMMON_NAME	DESCRIPTION	ELEVATION	FACC_CAT	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	VERT_ACC

VERT_DATUM	WIDTH

HS075	LANDING_PLACE	A named place, normally outside a harbor facility, where boats can transfer

passengers or cargo.  A ferry terminal may be called a landing area.

WIDTH

HS076	LANDMARK	Tall structures or objects which are precisely located to serve as an aid to naviations

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	DESIGNATOR	Directivity	ELEVATION	FORMAL_NAME	FUNCTION	HEIGHT	HORIZ_ACC

HORIZ_DATUM	PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SHAPE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS077	LEADING_LINE	A track line which passes through one or more (usually two) clearly defined objects, along which a vessel can safely travel.

DATE_END	DATE_START	DESCRIPTION	ORIENTATION	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS078	LEVEE	An embankment for controlling the waters of the sea, river or other water bodies.

COMMON_NAME	DESCRIPTION	RECORD_DATE	SOURCE_DATE

HS079	LIGHT_VESSEL/LIGHTSHIP	A distinctively marked manned vessel anchored or moored at a defined point to serve as an aid to navigation.

CHARACTER	COLOR_PATTERN	COMMON_NAME	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_DATUM	LENGTH

PERIOD	PRIMARY_COLOR	RANGE	RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS080	LOCK	A wet dock in a waterway, permitting a ship to pass from one level to another.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	DIRECTIVITY	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH	MATERIAL

RECORD_DATE	SOURCE_DATE	STATUS	WIDTH

HS081	LOCK_BASIN/LOCK_CHAMBER	A wet dock in a waterway, permitting a ship to pass from one level to another.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH	RECORD_DATE	SOURCE_DATE	STATUS	WIDTH

HS082	LOG_POND	A maritime area enclosed with connected floating timbers used as a staging area for sawn logs.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	LENGTH	RECORD_DATE	SOURCE_DATE	STATUS	WIDTH

HS083	MAGNETIC_DISTURBANCE_AREA	A localized anomaly in the earth's magnetic field.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	MAG_ANOMALY	RECORD_DATE	SOURCE_DATE

HS084	MAGNETIC_VARIATION	Lines connecting point of equal magnetic variation.

DATE_END	DATE_START	DESCRIPTION	RECORD_DATE	SOURCE_DATE	VARIATION

HS085	MAJOR_INFLOW/OUTFLOW_STRUCTUR	Major inflow and outflow structures, i.e., the intake structure of an electric generating stations, located in the river that are potential hazards to navigation.

COMMON_NAME	CONDITION	DATE_END	DATE_START	DEPTH	DESCRIPTION	FORMAL_NAME	HEIGHT	RECORD_DATE	RESTRICTION	S_57_CAT	SOURCE_DATE

STATUS	VERT_ACC	VERT_DATUM

HS086	MARINE_FARM	An assemblage of cages, nets, rafts and floats or posts where fish, including shellfish are artificially cultivated.

COMMON_NAME	DATE_END	DATE_START	DEPTH	DESCRIPTION	FORMAL_NAME	HEIGHT	RECORD_DATE	RESTRICTION	S_57_CAT	SOURCE_DATE	STATUS

VERT_ACC	VERT_DATUM	WIDTH

HS087	MAT_CASTING_FIELD	A site where concrete blocks are cast for ACM revetment.

COMMON_NAME	DATE_END	DATE_START		DESCRIPTION	FORMAL_NAME	RECORD_DATE		SOURCE_DATE	STATUS

HS088	MEASURED_DISTANCE_LINE	A course whose length has been accurately measured and is used in conjunction with ranges ashore.  It is used by vessels to calibrate logs, engine revolution counters, etc., and determine speed.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	LENGTH	ORIENTATION	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_DATUM

HS089	MILITARY_PRACTICE_AREA	An area within which naval, military or aerial exercises are carried out. Also called an exercise area.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	RESTRICTION	S_57_CAT	SOURCE_DATE	STATUS	WIDTH

HS090	MINE-NAVAL	An explosive device used in naval warfare located on or below the sea.

DEPTH	DESIGNATOR	HORIZ_ACC	IDENTIFIER	STATUS

HS091	MOORED_VESSEL	A semi-permanently moored ship.

COLOR_PATTERN	COMMON_NAME	CONDITION	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	LENGTH	PERMIT	PRIMARY_COLOR	RECORD_DATE	S_57_CAT

SOURCE_DATE	VERT_ACC	WIDTH

HS092	MOORING_FACILITY	A structure used for mooring/warping a ship or as a protection for harbor

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	PRIMARY_COLOR	RECORD_DATE	S_57_CAT

SHAPE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM

HS093	NAMED_WATER_AREA	An area within a water body which is commonly referenced by a name.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SEA_TYPE	SOURCE_DATE

HS094	NAVIGATION_LIGHT	A luminous or lighted aid to navigation.

CATEGORY	COLOR_PATTERN	COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_DATUM	MATERIAL

ORIENTATION	PRIMARY_COLOR	RANGE	RECORD_DATE	SIG_GROUP	SIG_PERIOD

SIQ_SEQUENCE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM

HS095	NAVIGATION_LINE	A navigation line is a straight line extending towards and area of navigational interest and generally generated by two navigational aids or one navigational aid and a bearing.

DATE_END	DATE_START	DESCRIPTION	ORIENTATION	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS096	OBSTRUCTION	In marine navigation, anything that hinders or prevents movement, particularly 	anything that endangers or prevents passage of a vessel. The term is usually used to  refer to an isolated danger to navigation…(IHO Dictionary, S-32, 5th Edition, 3503)

COMMON_NAME	CONDITION	CONSTRUCTION	DEPTH	DESCRIPTION	FORMAL_NAME	HEIGHT	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC

VERT_DATUM

HS097	OFFSHORE_LOADING_FACILITY	A facility located offshore for loading and unloading cargo.

COLOR_PATTERN	COMMON_NAME	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	PRIMARY_COLOR	RECORD_DATE	S_57_CAT

SHAPE	SOURCE_DATE	STATUS	VERT_ACC	VERT_LENGTH	WIDTH

HS098	OFFSHORE_PLATFORM	A permanent offshore structure, either fixed or floating, used in the production of oil or natural gas.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	ELEVATION

FORMAL_NAME	HEIGHT	HORIZ_ACC	PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS099	OFFSHORE_PRODUCTION_AREA	An area at sea within which there are production facilities.

COMMON_NAME	CONDITION	DATE_END	DATE_START	DEPTH	DESCRIPTION	FORMAL_NAME	HEIGHT	RECORD_DATE	RESTRICTION	S_57_CAT	SOURCE_DATE

STATUS	VERT_ACC	VERT_LENGTH	WIDTH

HS100	OIL_BARRIER	A construction to dam oil flow on water.

COMMON_NAME	CONDITION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS101	OVERHEAD_PIPELINE/CABLE	A collection of wires, cables, or pipe either supported or suspended above the waterway.

COMMON_NAME	CONDITION	DATE_END	DATE_START	DESCRIPTION	DESIGNATOR	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	LENGTH	MATERIAL

RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_CLEARANCE	VERT_DATUM	WIDTH

HS102	PARK	An area set aside and designated for several types of leisure or recreational activities.

COMMON_NAME

HS103	PARKING_AREA	An area used for parking vehicles not including residential streets and driveways.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	LENGTH	RECORD_DATE	S_57_CAT	SOURCE_DATE	SPACES	STATUS	WIDTH

HS104	PIER/WHARF/QUAY	A structure primarily used as berthing places for vessels.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE

LENGTH	PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS105	PILE/POST	A long heavy timber or section of steel, wood, concrete, etc.. forced into the earth which may serve as a support, as for a pier, or a free standing pole within a marine environment.

COLOR_PATTERN	COMMON_NAME	CONDITION	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	PRIMARY_COLOR	RECORD_DATE	S_57_CAT

SOURCE_DATE	VERT_ACC	VERT_DATUM	WIDTH

HS106	PILOT_BOARDING_PLACE	The meeting place to which a pilot comes out.

COMM_CHANNEL	COMMON_NAME	DATE_END	DATE_START	DEPTH	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	WIDTH

HS107	PONTOON	A permanently floating structure used as a bridge support or as the head of a pier, dock, or landing.

COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC

HS108	PORT_AUTHORITY	An area over which a harbour authorty has jurisdiction.

COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS109	PRECAUTIONARY_AREA	A routing measure comprising an area within defined limits where ships must navigate with particular caution and within which the direction of traffic flow may be recommended.

DATE_END	DATE_START	DEPTH	DESCRIPTION	FORMAL_NAME	RECORD_DATE	RESTRICTION	SOURCE_DATE	STATUS	WIDTH

HS110	PRODUCTION_AREA	An existing structure that was created, by man, for occupation, storage, or to facilitate  an activity.

COMMON_NAME	CONDITION	DATE_END	DATE_START	DESCRIPTION	DESIGNATOR	ELEVATION	FORMAL_NAME	FUNCTION	HEIGHT	HORIZ_ACC	HORIZ_DATUM

MATERIAL	PRODUCT	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM

WIDTH

HS111	PROMENADE_PIER	A pier used only for recreational purposes.  These structures are sometimes the remnants of the approaches to bridges.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE

LENGTH	PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS112	PYLON	A pylon or pole used to support a telephone or telegraph line.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_DATUM

PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	VERT_ACC	VERT_DATUM	WIDTH

HS113	RADAR_LINE	A track along which ships may be guided by coastal radar stations in the even of bad visibility.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	ORIENTATION	RECORD_DATE	SOURCE_DATE	STATUS

HS114	RADAR_RANGE	Indicates the coverage of a sea area by a radar surveillance station.  Inside this area a vessel may request shore based radar assistance, particularly in poor visibility.

COMM_CHANNEL	COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS

HS115	RADAR_REFLECTOR	A device capable of, or intended for, reflecting radar signals.

DESCRIPTION	HEIGHT	RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM

HS116	RADAR_STATION	A station with a transmitter emitting pulses of ultra-high frequency radio waves which are reflected by solid objects and are detected upon their return to the sending station.

COMM_CHANNEL	COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	LENGTH	MAX_RANGE	RECORD_DATE	S_57_CAT	SOURCE_DATE

STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS117	RADAR_TRANSPONDER_BEACON	A transponder beacon transmitting a coded signal on radar frequency, permitting an interrogating craft to determine the bearing and range of the transponder. Also called recon.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HORIZ_ACC	MAX_RANGE	PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE

STATUS

HS118	RADIO_CALLING_IN_POINT	A specified point some distance from the harbor at which a vessel's navigator notifies the harbor authority of his ship's position to assist traffic control.

COMM_CHANNEL	COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS

HS119	RADIO_STATION	A place equipped to transmit radio waves. Such a station may be either stationary or mobile, and may also be provided with a radio receiver.

CALL_SIGN	COMM_CHANNEL	COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	DESIGNATOR	ELEVATION	EST_RANGE	FORMAL_NAME	FREQUENCY	HORIZ_ACC

HORIZ_DATUM	LENGTH	MATERIAL	ORIENTATION	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	WIDTH

HS120	RAILROAD	A rail or set of parallel rails on which a train or tram runs.

COMMON_NAME	CONDITION	DESCRIPTION	FORMAL_NAME	HEIGHT	RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC

HS121	RAILROAD_YARD	A system of tracks within defined limits, and associated features, provided for loading/unloading and assembling trains.

COMMON_NAME	TRACK_LENGTH	WIDTH

HS122	RAPIDS	Portions of a stream with accelerated current where it descends rapidly but without a break in the slope of the bed sufficient to form a waterfall. Usually used in the plural.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	HEIGHT	RECORD_DATE	SOURCE_DATE	VERT_ACC	WIDTH

HS123	RECOMMENDED_TRACK	A track recommended to all or only certain vessels.

COMMON_NAME	DATE_END	DATE_START	DEPTH	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_DATUM

HS124	REEF	A rocky or coral elevation at or near enough to the surface of the sea to be a danger to surface navigation.

COMMON_NAME	DEPTH	DESCRIPTION	FORMAL_NAME	HORIZ_ACC	LENGTH	MATERIAL	RECORD_DATE	S_57_CAT	SOURCE_DATE	WIDTH

HS125	RESCUE_STATION	 A place at which life saving equipment is held.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	DESIGNATOR	ELEVATION	FORMAL_NAME	FUNCTION	HEIGHT	HORIZ_ACC	IDENTIFIER	LENGTH

MATERIAL	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	WIDTH

HS126	RESTRICTED_AREA	A specified area designated by an appropriate authority within which navigation is restricted in accordance with certain specified conditions.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	RESTRICTION	S_57_CAT	SOURCE_DATE	STATUS

HS127	RETRO_REFLECTOR	A means of distinguishing unlighted marks at night. Retro-reflective material is secured to the mark in a particular pattern to reflect back light.

COLOR_PATTERN	DESCRIPTION	HEIGHT	PRIMARY_COLOR	RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM

HS128	RIVER	A natural flowing watercourse.

COMMON_NAME	DEPTH	DESCRIPTION	FORMAL_NAME	LENGTH	RECORD_DATE	SOURCE_DATE	STATUS	WIDTH

HS129	RIVER_BANK	River edge delineated during general planimetric mapping from aerial photography.

COMMON_NAME	CONDITION	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE

HS130	RIVER_ENGINEERING_STRUCTURE	Any man-made object designed to check, control, or direct flow placed in the waterway which may pose a hazard to navigation.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH

PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS131	ROAD	A road is an open way for the passage of vehicles.

COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	DESIGNATOR	FORMAL_NAME	HORIZ_ACC	MATERIAL	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

SURFACE	WIDTH

HS132	RUNWAY	A defined area, usually rectangular, used for the conventional landing and take-off of aircraft.

COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	DESIGNATOR	ELEVATION	FORMAL_NAME	HORIZ_ACC	LENGTH	RECORD_DATE	S_57_CAT	SOURCE_DATE

STATUS	SURFACE	WIDTH

HS133	SAFETY_FAIRWAY	An area defined by the code of regulations where construction of temporary or permanent structures is prohibited.

COMMON_NAME	DATE_END	DATE_START	DEPTH	DESCRIPTION	FORMAL_NAME	RECORD_DATE	RESTRICTION	SOURCE_DATE	STATUS	VERT_DATUM

HS134	SAND_WAVES	A large mobile wave-like sediment feature in shallow water and composed of sand.  The wavelength may reach 1000 meters, the amplitude may be up to 20 meters.

DESCRIPTION	HEIGHT	RECORD_DATE	SOURCE_DATE	VERT_ACC

HS135	SANDBAR	The boundary or outline of an area where the bottom protrudes above the surface of the water subject to water levels and currents.

DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	VERT_DATUM

HS136	SEA-PLANE_LANDING_AREA	A designated portion of water for the landing and take-off  of sea planes.

COMMON_NAME	DESCRIPTION	ELEVATION	FORMAL_NAME	LENGTH	RECORD_DATE	RESTRICTION	SOURCE_DATE	STATUS	WIDTH

HS137	SEAWALL	A structure built to protect the shore from erosion.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH

PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS138	SHORELINE	The line where a land mass is in contact with a body of water.

COMMON_NAME	DESCRIPTION	ELEVATION	FACC_CAT	FORMAL_NAME	PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	VERT_ACC	VERT_DATUM

HS139	SHORELINE_CONSTRUCTION	Any man-made structure immediately adjacent to the water way designed to assist in the management of flow and the deposit of sediment.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE

LENGTH	PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM

WIDTH

HS140	SILO/TANK	A container used for the storage of liquids or gases.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	DESIGNATOR	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_DATUM	LENGTH

PRIMARY_COLOR	PRODUCT	RECORD_DATE	S_57_CAT	SHAPE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS141	SLIPWAY	A prepared slope for launching and recovering vessels.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH

PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS142	SLOPE_TOPLINE	The upper marking of a slope, e.g. the ridge line or the separation line between two different gradients.

COMMON_NAME	CONSTRUCTION	DESCRIPTION	ELEVATION	FORMAL_NAME	PRIMARY_COLOR	RECORD_DATE	S_57_CAT	SOURCE_DATE	VERT_ACC	VERT_DATUM

HS143	SMALL_CRAFT_FACILITY	A place at which a service generally of interest for small crafts or pleasure boats is available.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS144	SOUNDING	A measured water depth or spot depth which has been reduced to chart datum and includes drying heights.

COMMON_NAME	DEPTH	DESCRIPTION	FORMAL_NAME	HORIZ_ACC	RECORD_DATE	SOURCE_DATE	STATUS	VERT_DATUM

HS145	SPRING	A natural issue of water or other substances from the earth. One on the bottom of the sea is called a submarine spring.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE

HS146	STRAIGHT_TERRITORIAL_BASELINE	A baseline is the line from which the outer limits of the territorial sea and certain other outer limits are measured.

COMMON_NAME	COUNTRY	DESCRIPTION	RECORD_DATE	SOURCE_DATE

HS147	SUBMARINE_TRANSIT_LANE	An area where submarines may navigate under water or at the surface.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	RESTRICTION	SOURCE_DATE

HS148	SUBMERGED_PIPELINE/CABLE	Any pipeline or cable which lying on or under the bottom.

COMMON_NAME	CONDITION	DATE_END	DATE_START	DEPTH	DESCRIPTION	DESIGNATOR	DIAMETER	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC

HORIZ_DATUM	MATERIAL	PRODUCT	RECORD_DATE	RESTRICTION	S_57_CAT	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS149	SWAMP/MARSH	Those areas that are inundated or saturated by surface or ground water.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE

HS150	SWEPT_AREA	An area that has been determined to be clear of navigational dangers to a specified depth.

DEPTH	DESCRIPTION	RECORD_DATE	SOURCE_DATE	VERT_DATUM

HS151	TERRITORIAL_SEA_AREA	The territorial sea is a belt of water of a defined breadth but not exceeding 12 nautical 	miles measured seaward from the territorial sea baseline.

COMMON_NAME	COUNTRY	DESCRIPTION	RECORD_DATE	RESTRICTION	SOURCE_DATE	STATUS	WIDTH

HS152	TIDAL_STREAM	A tidal stream (or tidal current) is a horizontal movement of water associated with the rise and fall of the tide caused by tide-producing forces.

COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	MAX_RATE	MIN_RATE	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VELOCITY

HS153	TIDE_DATA_POINT	Tidal heights over time may be approximated by a series of height values given at regular intervals, starting from a specific moment in time.

COMMON_NAME	DESCRIPTION	FORMAL_NAME

RECORD_DATE	SOURCE_DATE	STATUS

TIME_START	TIME_END

HS154	TIDEWAY	A natural watercourse in intertidal areas where water flows during the ebb or flow.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE

HS155	TOP_MARK	One of more relatively small objects of characteric shape and color placed on an aid to identify it purpose.

COLOR_PATTERN	DESCRIPTION	HEIGHT	PRIMARY_COLOR	RECORD_DATE	SHAPE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM

HS156	TRAFFIC_SEPARATION_SCHEME	A traffic separation scheme is a scheme which aims to reduce the risk of collision in congested and/or converging areas by separating traffic moving in opposite, or nearly opposite, directions.

DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	RESTRICTION	S_57_CAT	SOURCE_DATE	STATUS

HS157	TUNNEL	A passage that is open at both ends, buried under the sea bed or laid over the sea floor or bored under the ground or through mountains. (based on ISO S-57)

COMMON_NAME	CONDITION	DESCRIPTION	FORMAL_NAME	HORIZ_ACC	HORIZ_CLEARANCE	LENGTH	RECORD_DATE	SOURCE_DATE	STATUS	VERT_ACC	VERT_CLEARANCE

WIDTH

HS158	TURNING_BASIN	A maintained area for vessels to turn.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	LENGTH	RECORD_DATE	RESTRICTION	SOURCE_DATE	VERT_DATUM	WIDTH

HS159	TWO_WAY_ROUTE	A two-way route is a route within defined limits inside which two-way traffic is established, aimed at providing safe passage of ships through waters where navigation is difficult or dangerous.(IHO Dictionary, S-32, 5th Edition, 5712)

COMMON_NAME	DATE_END	DATE_START	DEPTH	DESCRIPTION	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS	VERT_DATUM

HS160	UNDERWATER_ROCK	A concrete mass of stony material or coral which dries, is awash, or is below the water surface.

COMMON_NAME	DEPTH	DESCRIPTION	FORMAL_NAME	RECORD_DATE	SOURCE_DATE	STATUS	VERT_DATUM

HS161	UNSURVEYED_AREA	An area for which no bathymetric survey information is available.

COMMON_NAME	DESCRIPTION	RECORD_DATE	SOURCE_DATE	WIDTH

HS162	VEGETATION	Collections or individual plants.

COMMON_NAME	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	RECORD_DATE	S_57_CAT	SOURCE_DATE	VERT_ACC

HS163	VISUAL_SIGNAL_STATION	A place on shore from which signals are made to ships at sea.

COMM_CHANNEL	COMMON_NAME	DATE_END	DATE_START	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE	STATUS

HS164	WAITING_AREA/LOCK_ARRIVAL_POINT	A designated location where boats or tows wait to receive clearance to enter a lock chamber or basin.

HS165	WATER_TOWER	An elevated container and its supporting structure used to hold water.

COLOR_PATTERN	COMMON_NAME	CONDITION	CONSTRUCTION	DESCRIPTION	DESIGNATOR	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	HORIZ_DATUM	LENGTH	PRIMARY_COLOR	PRODUCT	RECORD_DATE	S_57_CAT	SHAPE	SOURCE_DATE	STATUS	VERT_ACC	VERT_DATUM	WIDTH

HS166	WATER_TURBULENCE	The disturbance of water caused by the interaction of any combination of waves, currents, tidal streams, wind, shoal patches and obstructions.

COMMON_NAME	DESCRIPTION	FORMAL_NAME	RECORD_DATE	S_57_CAT	SOURCE_DATE

HS167	WATERFALL	A sudden descent of water over a step in the bed of a river or the sea bottom caused by tidal flows. In place names commonly shortened to fall or falls, e.g. Niagara Falls.

COMMON_NAME	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	LENGTH	RECORD_DATE	SOURCE_DATE	VERT_ACC	WIDTH

HS168	WILDLIFE_MANAGEMENT_AREA	A area set aside for the investigation, maintenance, or management of plants and/or animals.

COMMON_NAME	DATE_END	DATE_START	DEPTH	DESCRIPTION	FORMAL_NAME	RECORD_DATE	RESTRICTION	S_57_CAT	SOURCE_DATE	STATUS	WIDTH

HS169	WRECK	The ruined remains of a stranded or sunken vessel which has been rendered useless.

COMMON_NAME	DATE_START	DEPTH	DESCRIPTION	ELEVATION	FORMAL_NAME	HEIGHT	HORIZ_ACC	LENGTH	RECORD_DATE	S_57_CAT	SOURCE_DATE

STATUS	TONNAGE	VERT_ACC	VERT_DATUM	WIDTH

5.0	HYDROGRAPHY STANDARD ATTRIBUTE DEFINITIONS

Attribute Name	           Attribute Definition	Data Type

BRIDGE_TYPE	The various types of bridges.	Text (30)

CALL_SIGN	The designated call-sign of a radio station.	Text (30)

CARDINAL	The four quadrants (north, east, south and west) are bounded	Text (35)

by the true bearings NW-NE, NE-SE, SE-SW, and SW-NW

taken from the point of interest.  A cardinal mark is named

after the quadrant in which it is placed.

CATEGORY	The attribute which differentiates the "types" or "kinds" of 	Text (35)

like features which may be separately identified in the

standard.  The specific values (or domain) associated with

the standard is a function of the individual feature type.

CHARACTER	Any identifier comprised of the class, number and color(s) of 	Text (30) flashes or occultations, of a light or lights at one geographic

position [i.e. Q(6)+LF1, VQ G, L F1 (3+2)WR].

CLEARANCE	The vertical clearance of an object in closed condition (e.g. a 	Text (30) closed lifting bridge) measured from the plane towards the object

overhead.

COLOR_PATTERN	The various colour patterns of a navigational mark.	Text (30)

COMM_CHANNEL	A channel number assigned to a specific radio frequency, 	Text (30) frequencies or frequency band.

COMMON_NAME	A unofficial, slang, or other common or textual designation of	Text (55)

the feature.

CONDITION	A domain value indicating the physical situation or condition of 	Text (35)  the feature.

CONSTRUCTION	A domain indicating the technique or primary method used in 	Text (35) building or constructing the feature.

COUNTRY	The attribute indicates the nationality of the specific object or 	Text (30) feature.

DATE_END	The date the feature will, or is expected to, cease to exist, if 	Numeric known.   May also indicate the latest date on which the feature

may reasonably be expected to be present in this location. This

date will almost always be in the future.

DATE_START	The date the existence of the feature began, if known. May also 	Numeric indicate the earliest date on which the feature may reasonably be

expected to be present in this location.

DEPTH	The numeric distance from the surface of the earth to the deepest Numeric point of the feature.

DEPTH_ACC	The best estimate of the accuracy of the sounding data	Text (30)

DEPTH_DATUM	The name of the datum which determines the reference for the 	Text (30) numeric attribute Depth.

DESCRIPTION	A user defined description of the feature.	Text (255)

DESIGNATOR	Any identifying number which differentiates the feature from any Numeric other similar features.

DIAMETER	Pipe diameter in inches	Numeric

DIRECTIVITY	The side or sides of a feature which produces the greatest 	Text (30) reflectivity potential.

ELEVATION	The altitude of the ground level of an object, measured from a 	Text (30) specified vertical datum.

EST_RANGE	The estimated range of a non-optical electromagnetic 	Text (30) transmission.

FACC_CAT	The differentiation attribute which exists within the Feature and 	Text (30) Attribute Coding Catalog Standard.

FORMAL_NAME	A official name or textual designation of the feature.	Text (55)

FREQUENCY	The frequency of a signal.	Text (30)

FUNCTION	The function, or purpose of various buildings.	Text (30)

HEIGHT	The numeric height of the feature as measured from the lowest 	Numeric

point to the highest point.

HORIZ_ACC	The best estimate of the horizontal accuracy of horizontal 	Numeric clearance and distances.

HORIZ_CLEARANCE	The numeric horizontal distance through an opening in the 	Numeric feature.

HORIZ_DATUM	Horizontal datum.  The name of the reference used for 	Text (30) measurements in the horizontal direction.

IDENTIFIER	A unique number which identifies the feature as opposed to all 	Text (30) other features of the same type.

LATERAL	There are two international buoyage regions, A and B, between 	Text (30) which lateral marks differ. The buoyage region is encoded using

the separate attribute MARSYS. When top-marks, retro reflectors

and/or lights are fitted to these marks, they are encoded as separate

objects.

LENGTH	A measurement of the longer of two linear axis.	Numeric

MAG_ANOMALY	The value of the deviation from the normal magnetic variation.	Numeric

MAG_VARIATION	Horizontal angle between true north and magnetic north 	Numeric measured East (positive value) or West (negative value) according

to whether magnetic north lies east or west of true north.

MATERIAL	A domain specifying the primary material used on the 	Text (35) construction of the feature.

MAX_RANGE	The extreme distance at which an object can be seen or a signal 	Numeric detected in nautical miles

MAX_RATE	Maximum speed of current.	Numeric

MIN_RATE	Minimum speed of current.	Numeric

NATURE_BOTTOM	The attribute ‘nature of surface’ encodes the general nature of 	Text (30)  the material of which the land surface or the sea bed is composed.

NO_FLOORS	The number of floors or levels within a structure.	Numeric

NUM_SPANS	Number of spans in a bridge or aqueduct.	Numeric

ORIENTATION	The angular distance measured from true north to the major axis 	Numeric     of the object.

PERIOD	The time occupied by an entire cycle of intervals of light and 	Text (30) eclipse.

PERMIT	Any permit required for the vessel.	Text (30)

PRIMARY_COLOR	The Primary or most frequently occurring color of the feature.	Text (12)

PRODUCT	The various substances which are transported, stored or 	Text (30) exploited.

QUALITY	The reliability of the value of sounding.	Text (30)

RADAR_REFLECTOR	Indicates whether or not a radar reflector is attached to, or 	Text (30) connected with, a feature.

RADIUS	The vector extending from the centre to the periphery of a 	Text (30) circular or spherical object.

RANGE	The nominal range at which an object can be seen or a signal 	Numeric detected in nautical miles.

RECORD_DATE	The date when the specific feature was captured, edited, or 	Numeric deleted.

RESTRICTION	A domain value indicating any limitations or other conditions 	Text (35) imposed on the use or function of the feature.

RIVER_MILE	The most currently used river mile designation for a given river 	Text (30) system.

S_57_CAT	The differentiation attribute which exists within the IHO S-57 	Text (30) Standard.

SEA_TYPE	The various types of sea areas.	Text (30)

SHAPE	The various types or shapes of the daymarkers used on beacons 	Text (30)   or buoys.

SIG_GROUP	The number of signals, the combination of signals or the morse 	Numeric character(s) within one period of full sequence.

SIG_PERIOD	The time occupied by an entire cycle of intervals of light and 	Text (30) eclipse.

SIQ_SEQUENCE	The sequence of times occupied by intervals of light and eclipse 	Text (30)  for all ‘light characteristics’ except for occulting where the

sequence of times is occupied by intervals of eclipse and light.

SOURCE_DATE	The production date of the source; e.g. the date of measurement.	Numeric

SPACES	The total parking spaces available in the area including 	Numeric handicapped or reserved spaces.

SPECIAL_PURPOSE	A mark may be a beacon, a buoy, a signpost or may take another 	Text (30) form.

STATUS	A domain value indicating the current status of the feature.	Text (35)

SURFACE	The physical surface composition of a road.	Text (30)

TIME_END	The end of a active period.	Numeric

TIME_START	The start of an active period.	Numeric

TONNAGE	Tonnage of a sunken or stranded wreck.	Numeric

TOP_MARK	The characteristic shape secured at the top of a buoy or beacon 	Text (30)    to aid identification.

TRACK_LENGTH	Total cumulative length of track contained within confines of 	Numeric   the feature, exclusive of the branch or main trunk lines running

into and/or out of the feature.

TRIP_LENGTH	Length of crossing between shore points.	Numeric

VARIATION	A positive value, i.e. unsigned indicates variation in an Easterly 	Numeric direction while a negative value indicates variation in a westerly

direction.

VELOCITY	The speed of the current in knots. The rate of travel of a current.	Numeric

VERT_ACC	The best estimate of the vertical accuracy of heights, vertical 	Numeric distances, and vertical clearances, excluding sounding

measurements.

VERT_CLEARANCE	The numeric distance from the surface of the earth to the lowest 	Numeric point associated with the feature.

VERT_DATUM	This attribute is used to specify the datum to which both heights 	Text (30) and soundings are referred.

VERT_LENGTH	The total vertical length of an object.	Numeric

WATER_VELOCITY	Range of water velocity, estimated in meters/second within 	Numeric  delineation of feature exclusive of high water due to runoff or

low water due to drought.

WIDTH	The numeric width of the feature as measured across its widest 	Numeric dimention.

6.0	IMPLEMENTATION

This Hydrography Standard has not yet been implemented in any significant way.    Its organization, however, is designed to permit easy implementation on a number of existing GIS and/or A-E-C/CADD platforms.  The conversion of the Hydrography Standard Logical Model to a physical implementation is accomplished by specifying several naming conventions associated with the standard.  These conventions and the physical implementation, while compatible with most major database management systems, are provided for information only and are not intended to mandate or recommend any vendors software.   In addition, the implementation strategy provided is only one of several acceptable strategies and is included for information only.  The revised organization of the Hydrography Standard and its naming conventions are represented in Figure 2.

Feature

(Graphic Symbology)

Primary Attribute Table

is described by

Figure 2

The codes of the features and the names of the attributes are designed to meet the naming restrictions associated with the major Relational Data Base Management Systems in use in the GIS field.  And, by defining standard “groupings” of attributes which apply to the features, it is possible to identify separate “tables” of these attributes associated with each of the features, further simplifying implementation.  The attribute groupings defined include IDENTIFICATION – which specifies numbers, names, and descriptions of the feature, FORM – which specifies physical characteristics of the features, and METADATA.

7.0	REFERENCES

International Hydrographic Organization, S57 Appendix A, Object Catalog for Digital Hydrographic Data, 1997.

National Institute of Standards and Technology, Federal Information Processing Standard Publication 173 (Spatial Data Transfer Standards), U. S. Department of Commerce, 1992.

North Atlantic Treaty Organization (NATO), Digital Geographic Information Exchange Standard (DIGEST) Part 4, Feature Attribute Coding Catalog (FACC), 1998.

Tri-Service CADD/GIS Technology Center, Tri-Service Spatial Data Standard (TSSDS), version 1.8, 1998.

U.S. Army Corps of Engineers (USACE), Regional Engineering and Environmental Geographic Information System (REEGIS), Project's Data Dictionary For Inland Waterways Information, 1997.

APPENDIX A1 - STANDARD CORRELATION OF S-57 (Feature Cross Reference) (INFORMATIVE)

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	S-57	S-57 CODE	S-57 ATTRIBUTE/VALUE

ADMINISTRATION_AREA	State	ADMINISTRATION AREA	ADMARE	JRSDTN - National Sub-Division

ADMINISTRATION_AREA	County	ADMINISTRATION AREA	ADMARE	JRSDTN - National Sub-Division

ADMINISTRATION_AREA	Coast Guard District	ADMINISTRATION AREA	ADMARE

ADMINISTRATION_AREA	COE District	ADMINISTRATION AREA	ADMARE

ADMINISTRATION_AREA	City	ADMINISTRATION AREA	ADMARE

AIRPORT/AIRFIELD	AIRPORT/AIRFIELD	AIRARE

ANCHOR_BERTH	ANCHOR BERTH	ACHBRT

ANCHORAGE_AREA	ANCHORAGE AREA	ACHARE

BEACON	BEACON	BCNLAT

BERTH	BERTH	BERTHS

BRIDGE	BRIDGE	BRIDGE

BUILDING	BUILDING, SINGLE	BUISGL

BUILT-UP_AREA	BUILT-UP AREA	BUAARE

BUOY	BUOY	BOYLAT

OFFSHORE_LOADING_FACILITY	BUOY, INSTALLATION	BOYINB	CATSEA - Single Buoy Mooring

OVERHEAD_PIPELINE/CABLE	CABLE AREA	CBLARE

OVERHEAD_PIPELINE/CABLE	Telephone Cable	CABLE, OVERHEAD	CBLOHD	CATCBL - Telephone

OVERHEAD_PIPELINE/CABLE	Electrical Cable	CABLE, OVERHEAD	CBLOHD	CATCBL - Transmission/Power

SUBMERGED_PIPELINE/CABLE	Electrical Cable	CABLE, SUBMARINE	CATCBL - Transmission/Power

SUBMERGED_PIPELINE/CABLE	Telephone Cable	CABLE, SUBMARINE	CATCBL - Telephone

CANAL	CANAL	CANALS

CARGO_TRANSHIPMENT_AREA	CARGO TRANSHIPMENT AREA	CTSARE

CAUSEWAY	CAUSEWAY	CAUSWY

CAUTION_AREA	CAUTION AREA	CTNARE

CHECKPOINT	CHECKPOINT	CHKPNT

COAST_GUARD_STATION	COAST GUARD STATION	CGUSTA

SHORELINE	COASTLINE	COALNE

CONTIGUOUS_ZONE	CONTIGUOUS ZONE	CONZNE

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	S-57	S-57 CODE	S-57 ATTRIBUTE/VALUE

CONTINENTAL_SHELF_AREA	CONTINENTAL SHELF AREA	COSARE

CONTROL_POINT	CONTROL POINT	CTRPNT

CONVEYOR	CONVEYOR	CONVYR

CRANE	CRANE	CRANES

CURRENT	CURRENT	CURENT

CUSTOM_ZONE	CUSTOM ZONE	CUSZNE

RIVER_ENGINEERING_STRUCTURE	Bendway Weir	DAM	SLCONS	CATDAM - Weir

DAM	DAM	DAMCON

DAY_MARK	DAY MARK	CAYMAR

DEEP_WATER_ROUTE	DEEP WATER ROUTE	DWRTCL

DEPTH_AREA	DEPTH AREA	DEPARE

DEPTH_CONTOUR	DEPTH CONTOUR	DEPCNT

DISTANCE_MARK	DISTANCE MARK	DISMAR

TURNING_BASIN	DREDGED AREA	DRGARE

DREDGED_AREA	DREDGED AREA	DRGARE

DRYDOCK	DRYDOCK	DRYDOC

DUMPING_GROUND	DUMPING GROUND	DMPGRD

LEVEE	DYKE	DYKCON

SAFETY_FAIRWAY	FAIRWAY	FAIRWY	RESTRN - Construction

CHANNEL_MAINTAINED(DEEP_DRAFT)	FAIRWAY	FAIRWY

FENCE/WALL	FENCE/WALL	FNCLNE

FERRY_ROUTE	FERRY ROUTE	FERYRT

FISHERY_ZONE	FISHERY ZONE	FSHZNE

FISHING_FACILITY	FISHING FACILITY	FSHFAC

FISHING_GROUND	FISHING GROUND	FSHGRD

FLOATING_DOCK	FLOATING DOCK	FLODOC

FOG_SIGNAL	FOG SIGNAL	FOGSIG

FORTIFIED_STRUCTURE	FORTIFIED STRUCTURE	FORSTC

FREEPORT_AREA	FREEPORT AREA	FRPARE

GATE	GATE	GATCON

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	S-57	S-57 CODE	S-57 ATTRIBUTE/VALUE

GRIDIRON	GRIDIRON	GRIDRN

PORT_AUTHORITY	HARBOR AREA	HRBFAC

HARBOR_FACILITY	HARBOR AREA (ADMINISTRATIVE)	HRBARE

FISHING_HARBOR	HARBOR FACILITY	HRBFAC	CATHAF - Fishing Harbour

HARBOR_FACILITY	HARBOR FACILITY	HRBFAC

MOORED_VESSEL	HULK	HULKES

ICE_AREA	ICE AREA	ICEARE

INCINERATION_AREA	INCINERATION AREA	ICNARE

INSHORE_TRAFFIC_ZONE	INSHORE TRAFFIC ZONE	ISTZNE

LAKE	LAKE	LAKARE

ISLAND	LAND AREA	LNDARE

ELEVATION	LAND ELEVATION	LNDELV

PARK	LAND REGION	CATLND - Parkland

SWAMP/MARSH	LAND REGION	LNDRGN	CATLND - Swamp

LANDMARK	Windmill/Motor	LANDMARK	LNDMRK	CATLMK - Windmill/Windmotor

LANDMARK	Smokestack/Chimney	LANDMARK	LNDMRK	CATLMK - Chimney

LANDMARK	Tower	LANDMARK	LNDMRK	CATLMK - Tower

LIGHT_VESSEL/LIGHTSHIP	LIGHT VESSEL	LITVES

NAVIGATION_LIGHT	LIGHTS	LIGHTS

MAGNETIC_DISTURBANCE_AREA	LOCAL MAGNETIC ANOMALY	LOCMAG

LOCK	LOCK BASIN	LOKBSN

LOCK_BASIN/LOCK_CHAMBER	LOCK BASIN	LOKBSN

LOG_POND	LOG POND	LOGPON

MAGNETIC_VARIATION	MAGNETIC VARIATION.	MAGVAR

MARINE_FARM	MARINE FARM/ CULTURE	MARCUL

MILITARY_PRACTICE_AREA	MILITARY PRACTICE AREA	MIPARE

GUIDE_WALL	MOORING FACILITY	SLCONS	CATMOR - Tie-Up Wall

DOLPHIN	MOORING/WARPING FACILITY	MORFAC	CATMOR - Dolphin

MOORING_FACILITY	MOORING/WARPING FACILITY	MORFAC

MOORING_FACILITY	Bollard	MOORING/WARPING FACILITY	MORFAC	CATMOR - Bollard

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	S-57	S-57 CODE	S-57 ATTRIBUTE/VALUE

LEADING_LINE	NAVIGATION LINE	NAVLNE

NAVIGATION_LINE	NAVIGATION LINE	NAVLNE

OBSTRUCTION	OBSTRUCTION/FOUL AREA	OBSTRN

FOUL_GROUND	OBSTRUCTION/FOUL AREA	OBSTRN	CATOBS - Foul Area

ICE_BOOM	OBSTRUCTION/FOUL AREA	OBSTRN	CATOBS - Ice Boom

OFFSHORE_PLATFORM	OFFSHORE PLATFORM	OFSPLF

OFFSHORE_PLATFORM	OFFSHORE PLATFORM	OFSPLF

OFFSHORE_PRODUCTION_AREA	OFFSHORE PRODUCTION AREA	OSPARE

OIL_BARRIER	OIL BARRIER	OILBAR

PILE/POST	PILE	PILPNT

PILOT_BOARDING_PLACE	PILOT BOARDING PLACE	PILBOP

SUBMERGED_PIPELINE/CABLE	PIPELINE SUBMARINE/ON LAND	PIPSOL

MAJOR_INFLOW/OUTFLOW_STRUCTURE	PIPELINE SUBMARINE/ON LAND	PIPSOL	CATPIP - Intake/Outfall

PONTOON	PONTOON	PONTON

PRECAUTIONARY_AREA	PRECAUTIONARY AREA	PRCARE

PRODUCTION_AREA	PRODUCTION/STORAGE AREA	PRDARE

BRIDGE_TOWER	PYLON/BRIDGE SUPPORT	PYLONS

BRIDGE_PIER	PYLON/BRIDGE SUPPORT	PYLONS

PYLON	PYLON/BRIDGE SUPPORT	PYLONS	CATPYL - Telephone/Telegraph

RADAR_LINE	RADAR LINE	RADLNE

RADAR_RANGE	RADAR RANGE	RADRNG

RADAR_REFLECTOR	RADAR REFLECTOR	RADRFL

RADAR_STATION	RADAR STATION	RADSTA

RADAR_TRANSPONDER_BEACON	RADAR TRANSPONDER BEACON	RTPBCN

RADIO_CALLING_IN_POINT	RADIO CALLING IN POINT	RDOCAL

RADIO_STATION	RADIO STATION	RDOSTA

RAILROAD	RAILWAY	RAILWY

RAPIDS	RAPIDS	RAPIDS

MEASURED_DISTANCE_LINE	RECOMMENDED TRACK/ PART	RECTRC

RECOMMENDED_TRACK	RECOMMENDED TRACK/ PART	RECTRC

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	S-57	S-57 CODE	S-57 ATTRIBUTE/VALUE

RESCUE_STATION	RESCUE STATION	RSCSTA

WILDLIFE_MANAGEMENT_AREA	Marine Sanctuary	RESTRICTED AREA	RESARE	CATREA - Fish Sanctuary

WILDLIFE_MANAGEMENT_AREA	Federal	RESTRICTED AREA	CATRES - Ecological Reserve

WILDLIFE_MANAGEMENT_AREA	State	RESTRICTED AREA	CATRES - Ecological Reserve

RESTRICTED_AREA	RESTRICTED AREA	RESARE

RETRO_REFLECTOR	RETRO REFLECTOR	RETRFL

RIVER	RIVER	RIVERS

RIVER_BANK	RIVER BANK	RIVBNK

ROAD	ROAD	ROADWY

RUNWAY	RUNWAY	RUNWAY

SAND_WAVES	SAND WAVES	SNDWAV

NAMED_WATER_AREA	Lagoon/Reef Pool	SEA AREA/NAMED WATER AREA	SEAARE	CATSEA - Not specifically

REEF	SEA AREA/NAMED WATER AREA	SEAARE	CATSEA - REEF

NAMED_WATER_AREA	Crossing	SEA AREA/NAMED WATER AREA	SEAARE	CATSEA - Not specifically

NAMED_WATER_AREA	Chute	SEA AREA/NAMED WATER AREA	SEAARE	CATSEA - Not specifically

SEA-PLANE_LANDING_AREA	SEA-PLANE LANDING AREA	SPLARE

SANDBAR	SEABED AREA	DEPARE	NATSUR - Sand

BOTTOM_CHARACTERISTICS	SEABED AREA.	SBDARE

SLIPWAY	SHORELINE CONSTRUCTION	SLCONS	CATSLC - Slipway

PROMENADE_PIER	SHORELINE CONSTRUCTION	SLCONS	CATSLC - Promenade Pier

BOAT_RAMP	SHORELINE CONSTRUCTION	SLCONS	CATSLC   Ramp

PIER/WHARF/QUAY	SHORELINE CONSTRUCTION	SLCONS	CATSLC  Wharf (Quay)

FENDER	SHORELINE CONSTRUCTION	SLCONS	CATSLC - Fender

SEAWALL	SHORELINE CONSTRUCTION	SLCONS	CATSLC - Sea Wall

SHORELINE_CONSTRUCTION	ACM Revetment Composite	SHORELINE CONSTRUCTION	SLCONS	CATSLC - Revetment

SHORELINE_CONSTRUCTION	Stone Bank Paving	SHORELINE CONSTRUCTION	SLCONS	CATSLC - RipRap

SHORELINE_CONSTRUCTION	Groin	SHORELINE CONSTRUCTION	SLCONS	CATSLC - Groyne

DYKE	SHORELINE CONSTRUCTION	DYKCON	CATSLS - Training Wall

SHORELINE_CONSTRUCTION	Mole	SHORELINE CONSTRUCTION	SLCONS	CATSLC - Mole

BREAKWATER	SHORELINE CONSTRUCTION	SLCONS	CATSLC   Break Water

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	S-57	S-57 CODE	S-57 ATTRIBUTE/VALUE

GAUGING_STATION	SIGNAL STATION, WARNING	SISTAW	CATSIW - Tide Gauge

VISUAL_SIGNAL_STATION	SIGNAL STATION,TRAFFIC	SISTAT

SILO/TANK	SILO/TANK	SILTNK

GRAIN_ELEVATOR/ELEVATOR	SILO/TANK	SILTNK	CATSIL - Grain Elevator

WATER_TOWER	SILO/TANK	SILTNK	CATSIL - Water Tower

SLOPE_TOPLINE	SLOPE TOPLINE	SLOTOP

LANDING_PLACE	SMALL CRAFT FACILITY	CATSCF - Landing

PARKING_AREA	SMALL CRAFT FACILITY	SMCFAC	CATSCF - CAR PARK

SMALL_CRAFT_FACILITY	SMALL CRAFT FACILITY	SMCFAC

SOUNDING	SOUNDING	SOUNDG

SPRING	SPRING	SPRING

STRAIGHT_TERRITORIAL_BASELINE	STRAIGHT TERRITORIAL BASELINE	STSLNE

SUBMARINE_TRANSIT_LANE	SUBMARINE TRANSIT LANE	SUBTLN

SWEPT_AREA	SWEPT AREA	SWPARE

TERRITORIAL_SEA_AREA	TERRITORIAL SEA AREA	TESARE

TIDAL_STREAM	TIDAL STREAM - FLOOD/EBB	TS_FEB

TIDE_DATA_POINT	TIDE -TIME SERIES	T_TIMS

TIDEWAY	TIDEWAY	TIDEWY

TOP_MARK	TOP MARK	TOPMAR

TRAFFIC_SEPARATION_SCHEME	TRAFFIC SEPARATION SCHEME	TSSBND

TUNNEL	TUNNEL	TUNNEL

TWO_WAY_ROUTE	TWO-WAY ROUTE PART	TWRTPT

UNDERWATER_ROCK	UNDERWATER ROCK	UWTROC

UNSURVEYED_AREA	UNSURVEYED AREA	UNSARE

VEGETATION	VEGETATION	VEGATN

WATER_TURBULENCE	WATER TURBULENCE	WATTUR

WATERFALL	WATERFALL	WATFAL

AQUATIC_VEGETATION_AREA	WEED/KELP	WEDKLP

WRECK	WRECK	WRECKS

APPENDIX A2 - STANDARD CORRELATION OF S-57 (Attribute Cross Reference) (INFORMATIVE)

ADMINISTRATION_AREA	HS001

INFORM	Information	DESCRIPTION

JRSDTN	Jurisdiction	CATEGORY

NATION	Nationality	COUNTRY

OBJNAM	Object name	FORMAL_NAME

OBJNAM	Object name in national language	COMMON_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

AIRPORT/AIRFIELD	HS002

CONDTN	Condition	CONDITION

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

ANCHOR_BERTH	HS003

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RADIUS	Radius	RADIUS

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

ANCHORAGE_AREA	HS004

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

AQUATIC_VEGETATION_AREA	HS005

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

BEACON	HS006

BCNSHP	Beacon shape	SHAPE

CATCAM	Category of cardinal mark	CARDINAL

CATLAM	Category of lateral mark	LATERAL

CATSPM	Category of special purpose mark	SPECIAL_PURPO

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

ELEVAT	Elevation	ELEVATION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

BERTH	HS007

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

QUASOU	Quality of sounding measurement	QUALITY

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

SOUACC	Sounding accuracy	DEPTH_ACC

STATUS	Status	STATUS

VERDAT	Vertical datum	DEPTH_DATUM

BOAT_RAMP	HS009

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

VERLEN	Vertical length	VERT_LENGTH

BOTTOM_CHARACTERISTICS	HS010

COLOUR	Colour	PRIMARY_COLOR

INFORM	Information	DESCRIPTION

NATSUR	Nature of surface	NATURE_BOTTOM

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

BREAKWATER	HS011

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

VERLEN	Vertical length	VERT_LENGTH

BRIDGE	HS012

CATBRG	Category of bridge	BRIDGE_TYPE

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERCCL	Vertical clearance, closed	CLEARANCE

VERCLR	Vertical clearance	VERT_CLEARANC

VERDAT	Vertical datum	VERT_DATUM

BRIDGE_PIER	HS013

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

VERLEN	Vertical length	VERT_LENGTH

BRIDGE_TOWER	HS014

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

VERLEN	Vertical length	VERT_LENGTH

BUILDING	HS015

BUISHP	Building shape	SHAPE

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

ELEVAT	Elevation	ELEVATION

FUNCTN	Function+	FUNCTION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

VERLEN	Vertical length	LENGTH

BUILT-UP_AREA	HS016

CATBUA	Category of built-up area	S_57_CAT

CONDTN	Condition	CONDITION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

BUOY	HS017

BOYSHP	Buoy shape	SHAPE

CATCAM	Category of cardinal mark	S_57_CAT

CATLAM	Category of lateral mark	LATERAL

CATSPM	Category of special purpose mark	SPECIAL_PURPO

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERLEN	Vertical length	HEIGHT

CANAL	HS018

CATCAN	Category of canal	S_57_CAT

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

CARGO_TRANSHIPMENT_AREA	HS019

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

CAUSEWAY	HS020

CONDTN	Condition	CONDITION

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

CAUTION_AREA	HS021

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

CHANNEL_MAINTAINED(DEEP_DRAF	HS023

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

SOUACC	Sounding accuracy	DEPTH_ACC

STATUS	Status	STATUS

VERDAT	Vertical datum	VERT_DATUM

COAST_GUARD_STATION	HS025

CATCHP	Category of checkpoint	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

CONTIGUOUS_ZONE	HS026

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NATION	Nationality	COUNTRY

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

CONTINENTAL_SHELF_AREA	HS027

INFORM	Information	DESCRIPTION

NATION	Nationality	COUNTRY

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

CONTROL_POINT	HS028

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

ELEVAT	Elevation	ELEVATION

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

CONVEYOR	HS029

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERCLR	Vertical clearance	VERT_CLEARANC

VERDAT	Vertical datum	VERT_DATUM

CRANE	HS030

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERCLR	Vertical clearance	VERT_CLEARANC

VERDAT	Vertical datum	VERT_DATUM

CURRENT	HS031

CURVEL	Current velocity	VELOCITY

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

ORIENT	Orientation	ORIENTATION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

CUSTOM_ZONE	HS032

INFORM	Information	DESCRIPTION

NATION	Nationality	COUNTRY

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

DAM	HS033

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

DAY_MARK	HS034

CATSPM	Category of special purpose mark	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

ELEVAT	Elevation	ELEVATION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

TOPSHP	Topmark/daymark shape	SHAPE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

DEEP_WATER_ROUTE	HS035

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

SOUACC	Sounding accuracy	DEPTH_ACC

STATUS	Status	STATUS

VERDAT	Vertical datum	VERT_DATUM

DEPTH_AREA	HS036

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERDAT	Vertical datum	VERT_DATUM

DEPTH_CONTOUR	HS037

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VALDCO	Value of depth contour	DEPTH

VERDAT	Vertical datum	VERT_DATUM

DISTANCE_MARK	HS038

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

DOLPHIN	HS039

BOYSHP	Buoy shape	SHAPE

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

DREDGED_AREA	HS040

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

VERDAT	Vertical datum	VERT_DATUM

DRYDOCK	HS041

CONDTN	Condition	CONDITION

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERDAT	Vertical datum	VERT_DATUM

DUMPING_GROUND	HS042

CATDPG	Category of dumping ground	S_57_CAT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

DYKE	HS043

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

ELEVATION	HS044

ELEVAT	Elevation	ELEVATION

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

FENCE/WALL	HS046

CATFNC	Category of fenceline	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

ELEVAT	Elevation	ELEVATION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

FENDER	HS047

CATSLC	Category of shoreline construction	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

FERRY_ROUTE	HS048

CATFRY	Category of ferry	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

FISHERY_ZONE	HS049

INFORM	Information	DESCRIPTION

NATION	Nationality	COUNTRY

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

FISHING_FACILITY	HS050

CATFIF	Category of fishing facility	S_57_CAT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERLEN	Vertical length	HEIGHT

FISHING_GROUND	HS051

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

FISHING_HARBOR	HS052

CATHAF	Category of harbour facility	S_57_CAT

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

FLOATING_DOCK	HS054

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

VERLEN	Vertical length	HEIGHT

FLOODWALL	HS056

CATSLC	Category of shoreline construction	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

FOG_SIGNAL	HS057

CATFOG	Category of fog signal	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SIGFRQ	Signal frequency	FREQUENCY

SIGPER	Signal period	PERIOD

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

FORTIFIED_STRUCTURE	HS058

CATFOR	Category of fortified structure	S_57_CAT

CONDTN	Condition	CONDITION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

FOUL_GROUND	HS059

CATOBS	Category of obstruction	S_57_CAT

CONDTN	Condition	CONDITION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VALSOU	Value of sounding	DEPTH

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

FREEPORT_AREA	HS060

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

GATE	HS061

CATGAT	Category of gate	S_57_CAT

CONDTN	Condition	CONDITION

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERCLR	Vertical clearance	VERT_CLEARANC

VERDAT	Vertical datum	VERT_DATUM

GAUGING_STATION	HS062

CATSIW	Category of signal station, warning	S_57_CAT

COMCHA	Communication channel	COMM_CHANNEL

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

GRAIN_ELEVATOR/ELEVATOR	HS063

BUISHP	Building shape	SHAPE

CATSIL	Category of silo/tank	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

ELEVAT	Elevation	ELEVATION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

GRIDIRON	HS064

HORACC	Horizontal accuracy	HORIZ_ACC

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERLEN	Vertical length	HEIGHT

GUIDE_WALL	HS065

CATSLC	Category of shoreline construction	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

HARBOR	HS066

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

HARBOR_FACILITY	HS067

CATHAF	Category of harbour facility	S_57_CAT

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

ICE_AREA	HS068

CATICE	Category of ice	S_57_CAT

ELEVAT	Elevation	ELEVATION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

ICE_BOOM	HS069

CATOBS	Category of obstruction	S_57_CAT

CONDTN	Condition	CONDITION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VALSOU	Value of sounding	DEPTH

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

INCINERATION_AREA	HS070

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

INSHORE_TRAFFIC_ZONE	HS071

CATTSS	Category of Traffic Separation Scheme	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

ISLAND	HS072

CONDTN	Condition	CONDITION

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

LAKE	HS074

ELEVAT	Elevation	ELEVATION

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

LANDMARK	HS076

CATLMK	Category of landmark	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

ELEVAT	Elevation	ELEVATION

FUNCTN	Function+	FUNCTION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

LEADING_LINE	HS077

CATNAV	Category of navigation line	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

ORIENT	Orientation	ORIENTATION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

LEVEE	HS078

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

LIGHT_VESSEL/LIGHTSHIP	HS079

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HORACC	Horizontal accuracy	HORIZ_ACC

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

LOCK	HS080

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

LOCK_BASIN/LOCK_CHAMBER	HS081

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

LOG_POND	HS082

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

MAGNETIC_DISTURBANCE_AREA	HS083

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VALLMA	Value of local magnetic anomaly	MAG_ANOMALY

MAGNETIC_VARIATION	HS084

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VALMAG	Value of magnetic variation	VARIATION

MAJOR_INFLOW/OUTFLOW_STRUCT	HS085

BURDEP	Buried depth	DEPTH

CATPIP	Category of pipeline/pipe	S_57_CAT

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

VERLEN	Vertical length	HEIGHT

MARINE_FARM	HS086

CATMFA	Category of marine farm/culture	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VALSOU	Value of sounding	DEPTH

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

VERLEN	Vertical length	HEIGHT

MEASURED_DISTANCE_LINE	HS088

CATTRK	Category of recommended track	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

ORIENT	Orientation	ORIENTATION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERDAT	Vertical datum	VERT_DATUM

MILITARY_PRACTICE_AREA	HS089

CATMPA	Category of military practice area	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

MOORED_VESSEL	HS091

CATHLK	Category of hulk	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

HORACC	Horizontal accuracy	HORIZ_ACC

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERLEN	Vertical length	HEIGHT

MOORING_FACILITY	HS092

BOYSHP	Buoy shape	SHAPE

CATMOR	Category of mooring/warping facility	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

NAMED_WATER_AREA	HS093

CATSEA	Category of sea area	SEA_TYPE

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

NAVIGATION_LIGHT	HS094

CATLIT	Category of light	CATEGORY

COLOUR	Colour	PRIMARY_COLOR

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

ORIENT	Orientation	ORIENTATION

RECDAT	Recording date	RECORD_DATE

SECTR1	Sector limit one	Sector limit one

SECTR2	Sector limit two	Sector limit two

SIGGRP	Signal group	SIG_GROUP

SIGPER	Signal period	SIG_PERIOD

SIGSEQ	Signal sequence	SIQ_SEQUENCE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VALNMR	Value of nominal range	RANGE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

NAVIGATION_LINE	HS095

CATNAV	Category of navigation line	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

ORIENT	Orientation	ORIENTATION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

OBSTRUCTION	HS096

CATOBS	Category of obstruction	S_57_CAT

CONDTN	Condition	CONDITION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VALSOU	Value of sounding	DEPTH

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

OFFSHORE_LOADING_FACILITY	HS097

BOYSHP	Buoy shape	SHAPE

CATINB	Category of installation buoy	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERLEN	Vertical length	VERT_LENGTH

OFFSHORE_PLATFORM	HS098

CATOFP	Category of offshore platform	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

OFFSHORE_PRODUCTION_AREA	HS099

CATPRA	Category of production area	S_57_CAT

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERLEN	Vertical length	VERT_LENGTH

OIL_BARRIER	HS100

CATOLB	Category of oil barrier	S_57_CAT

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

OVERHEAD_PIPELINE/CABLE	HS101

CATCBL	Category of cable	S_57_CAT

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERCLR	Vertical clearance	VERT_CLEARANC

VERDAT	Vertical datum	VERT_DATUM

PARKING_AREA	HS103

CATSCF	Category of small craft facility	S_57_CAT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

PIER/WHARF/QUAY	HS104

CATSLC	Category of shoreline construction	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

PILE/POST	HS105

CATPLE	Category of pile	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

PILOT_BOARDING_PLACE	HS106

CATPIL	Category of pilot boarding place	S_57_CAT

COMCHA	Communication channel	COMM_CHANNEL

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

PONTOON	HS107

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERLEN	Vertical length	HEIGHT

PORT_AUTHORITY	HS108

CATHAF	Category of harbour facility	S_57_CAT

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

PRECAUTIONARY_AREA	HS109

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

PRODUCTION_AREA	HS110

CATPRA	Category of production area	S_57_CAT

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

ELEVAT	Elevation	ELEVATION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

PRODCT	Product	PRODUCT

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

PROMENADE_PIER	HS111

CATSLC	Category of shoreline construction	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

PYLON	HS112

CATPYL	Category of pylon	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

FEATURE NAME

RADAR_LINE	HS113

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

ORIENT	Orientation	ORIENTATION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

RADAR_RANGE	HS114

COMCHA	Communication channel	COMM_CHANNEL

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

RADAR_REFLECTOR	HS115

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

RADAR_STATION	HS116

CATRAS	Category of radar station	S_57_CAT

COMCHA	Communication channel	COMM_CHANNEL

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VALMXR	Value of maximum range	MAX_RANGE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

RADAR_TRANSPONDER_BEACON	HS117

CATRTB	Category of radar transponder beacon	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VALMXR	Value of maximum range	MAX_RANGE

RADIO_CALLING_IN_POINT	HS118

COMCHA	Communication channel	COMM_CHANNEL

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

RADIO_STATION	HS119

CALSGN	Call sign	CALL_SIGN

CATROS	Category of radio station	S_57_CAT

COMCHA	Communication channel	COMM_CHANNEL

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

ESTRNG	Estimated range of transmission	EST_RANGE

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

ORIENT	Orientation	ORIENTATION

RECDAT	Recording date	RECORD_DATE

SIGFRQ	Signal frequency	FREQUENCY

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

RAILROAD	HS120

CONDTN	Condition	CONDITION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

RAPIDS	HS122

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERLEN	Vertical length	HEIGHT

RECOMMENDED_TRACK	HS123

CATTRK	Category of recommended track	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERDAT	Vertical datum	VERT_DATUM

REEF	HS124

CATSEA	Category of sea area	S_57_CAT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

RESCUE_STATION	HS125

CATRSC	Category of rescue station	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

RESTRICTED_AREA	HS126

CATREA	Category of restricted area	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

RETRO_REFLECTOR	HS127

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

RIVER	HS128

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

RIVER_BANK	HS129

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

RIVER_ENGINEERING_STRUCTURE	HS130

CATSLC	Category of shoreline construction	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

ROAD	HS131

CATROD	Category of road	S_57_CAT

CONDTN	Condition	CONDITION

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

RUNWAY	HS132

CATRUN	Category of runway	S_57_CAT

CONDTN	Condition	CONDITION

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

SAFETY_FAIRWAY	HS133

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERDAT	Vertical datum	VERT_DATUM

SAND_WAVES	HS134

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERLEN	Vertical length	HEIGHT

SANDBAR	HS135

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERDAT	Vertical datum	VERT_DATUM

SEA-PLANE_LANDING_AREA	HS136

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

SEAWALL	HS137

CATSLC	Category of shoreline construction	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

SHORELINE	HS138

CATCOA	Category of coastline	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

ELEVAT	Elevation	ELEVATION

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

SHORELINE_CONSTRUCTION	HS139

CATSLC	Category of shoreline construction	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

SILO/TANK	HS140

BUISHP	Building shape	SHAPE

CATSIL	Category of silo/tank	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

ELEVAT	Elevation	ELEVATION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

PRODCT	Product	PRODUCT

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

SLIPWAY	HS141

CATSLC	Category of shoreline construction	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

HEIGHT	Height	HEIGHT

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

HORLEN	Horizontal length	LENGTH

HORWID	Horizontal width	WIDTH

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

SLOPE_TOPLINE	HS142

CATSLO	Category of slope	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

ELEVAT	Elevation	ELEVATION

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

SMALL_CRAFT_FACILITY	HS143

CATSCF	Category of small craft facility	S_57_CAT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

SOUNDING	HS144

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERDAT	Vertical datum	VERT_DATUM

SPRING	HS145

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STRAIGHT_TERRITORIAL_BASELINE	HS146

INFORM	Information	DESCRIPTION

NATION	Nationality	COUNTRY

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

SUBMARINE_TRANSIT_LANE	HS147

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

SUBMERGED_PIPELINE/CABLE	HS148

BURDEP	Buried depth	DEPTH

CATCBL	Category of cable	S_57_CAT

CONDTN	Condition	CONDITION

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

PRODCT	Product	PRODUCT

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

VERLEN	Vertical length	HEIGHT

SWAMP/MARSH	HS149

CATLND	Category of land region	S_57_CAT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

SWEPT_AREA	HS150

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERDAT	Vertical datum	VERT_DATUM

TERRITORIAL_SEA_AREA	HS151

INFORM	Information	DESCRIPTION

NATION	Nationality	COUNTRY

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

TIDAL_STREAM	HS152

CAT_TS	Category of Tidal stream	S_57_CAT

CURVEL	Current velocity	VELOCITY

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

T_ACWL	Tide - accuracy of water level	Tide - accuracy of

T_MTOD	Tide - method of tidal prediction	Tide - method of

T_THDF	Tide - time and height differences	Tide - time and

T_TINT	Tide - time interval of values	Tide - time interval

T_TSVL	Tide - time series values	Tide - time series

T_VAHC	Tide - value of harmonic constituents	Tide - value of

TIMEND	Time end	Time end

TIMSTA	Time start	Time start

TS_TSP	Tidal stream - panel values	Tidal stream - panel

TIDE_DATA_POINT	HS153

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

T_ACWL	Tide - accuracy of water level	Tide - accuracy of

T_HWLW	Tide - high and low water values	Tide - high and low

T_MTOD	Tide - method of tidal prediction	Tide - method of

T_THDF	Tide - time and height differences	Tide - time and

T_TINT	Tide - time interval of values	Tide - time interval

T_VAHC	Tide - value of harmonic constituents	Tide - value of

TIMEND	Time end	Time end

TIMSTA	Time start	Time start

TS_TSV	Tidal stream - time series values	Tidal stream - time

TIDEWAY	HS154

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

TOP_MARK	HS155

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

TOPSHP	Topmark/daymark shape	SHAPE

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

TRAFFIC_SEPARATION_SCHEME	HS156

CATTSS	Category of Traffic Separation Scheme	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

TUNNEL	HS157

CONDTN	Condition	CONDITION

HORACC	Horizontal accuracy	HORIZ_ACC

HORCLR	Horizontal clearance	HORIZ_CLEARAN

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERCLR	Vertical clearance	VERT_CLEARANC

TURNING_BASIN	HS158

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

VERDAT	Vertical datum	VERT_DATUM

TWO_WAY_ROUTE	HS159

CATTRK	Category of recommended track	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERDAT	Vertical datum	VERT_DATUM

UNDERWATER_ROCK	HS160

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VALSOU	Value of sounding	DEPTH

VERDAT	Vertical datum	VERT_DATUM

UNSURVEYED_AREA	HS161

INFORM	Information	DESCRIPTION

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VEGETATION	HS162

CATVEG	Category of vegetation	S_57_CAT

ELEVAT	Elevation	ELEVATION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

VISUAL_SIGNAL_STATION	HS163

CATSIT	Category of signal station, traffic	S_57_CAT

COMCHA	Communication channel	COMM_CHANNEL

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

WATER_TOWER	HS165

BUISHP	Building shape	SHAPE

CATSIL	Category of silo/tank	S_57_CAT

COLOUR	Colour	PRIMARY_COLOR

COLPAT	Colour pattern	COLOR_PATTERN

CONDTN	Condition	CONDITION

ELEVAT	Elevation	ELEVATION

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NATCON	Nature of construction	CONSTRUCTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

PRODCT	Product	PRODUCT

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

WATER_TURBULENCE	HS166

CATWAT	Category of water turbulence	S_57_CAT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

WATERFALL	HS167

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

VERACC	Vertical accuracy	VERT_ACC

WILDLIFE_MANAGEMENT_AREA	HS168

CATREA	Category of restricted area	S_57_CAT

DATEND	Date end	DATE_END

DATSTA	Date start	DATE_START

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

RESTRN	Restriction	RESTRICTION

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

WRECK	HS169

CATWRK	Category of wreck	S_57_CAT

HEIGHT	Height	HEIGHT

INFORM	Information	DESCRIPTION

NOBJNM	Object name in national language	COMMON_NAME

OBJNAM	Object name	FORMAL_NAME

RECDAT	Recording date	RECORD_DATE

SORDAT	Source date	SOURCE_DATE

STATUS	Status	STATUS

VALSOU	Value of sounding	DEPTH

VERACC	Vertical accuracy	VERT_ACC

VERDAT	Vertical datum	VERT_DATUM

APPENDIX B1 - STANDARD CORRELATION OF FACC (Feature Cross Reference) (INFORMATIVE)

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	FACC	FACC CODE	FACC ATTRIBUTE/VALUE

ADMINISTRATION_AREA	State	ADMINISTRATION_AREA_(NAMED)	FA001	USE - 5  State

ADMINISTRATION_AREA	County	ADMINISTRATION_AREA_(NAMED)	FA001	USE -

ADMINISTRATION_AREA	City	ADMINISTRATION_AREA_(NAMED)	FA001	USE 16 -City

AIRPORT/AIRFIELD	AIRPORT_AREA	GB007	APT -14 Airport/Airfield

ANCHOR_BERTH	ANCHOR_BERTH	BB012	MAC -12 Anchoring Berths

ANCHORAGE_AREA	ANCHORAGE	BB101	MAC -11 Anchorage

RADAR_TRANSPONDER_BEACON	BEACON	BC010	NST - 10 Radar Responder

BEACON	BEACON	BC010

CONTROL_POINT	BENCHMARK	ZB020

BERTH	BERTH	BB020

BOAT_LIFT	BOAT_LIFT	BI005

TURNING_BASIN	BOAT_TURNING_BASIN	BI080

MOORING_FACILITY	Bollard	BOLLARD	BB030

BOTTOM_CHARACTERISTICS	BOTTOM_CHARACTERISTICS	BF010

SLOPE_TOPLINE	BREAKLINE	CA026

BREAKWATER	BREAKWATER	BB041

BRIDGE	BRIDGE	AQ040

BRIDGE_PIER	BRIDGE_PIER	AQ056

BRIDGE_TOWER	BRIDGE_TOWER	AQ055

PRODUCTION_AREA	BUILDING	AL015	BFC - Oil/Gas Facilities Building

RESCUE_STATION	BUILDING	AL015	STA - 5 LifeBoat/Rescue

BUILDING	BUILDING	AL015	BFC - 16 House

BUILDING	BUILDING	AL015	BFC - 17 Multi Unit Dwelling

BUILT-UP_AREA	BUILT-UP_AREA	AL020

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	FACC	FACC CODE	FACC ATTRIBUTE/VALUE

BUOY	BUOY	BC020

RADIO_CALLING_IN_POINT	CALLING-IN_POINT	BB050

CANAL	CANAL	BH020

CAUSEWAY	CAUSEWAY	AQ064

CHECKPOINT	CHECKPOINT	AH070

LANDMARK	Smokestack/Chimney	CHIMNEY	AF010

SHORELINE	COASTLINE	BA010

RADIO_STATION	COMMUNICATION BUILDING	AT080

CONVEYOR	CONVEYOR	AF020

CRANE	CRANE	AF040

SUBMERGED_PIPELINE/CABLE	CULVERT	AQ065

TIDAL_STREAM	CURRENT_FLOW	BG010	CUR - 3 General Flow

DAM	DAM	BI020

DEPTH_AREA	DEPTH_AREA	BE019

DEPTH_CONTOUR	DEPTH_CONTOUR	BE015

DISTANCE_MARK	DISTANCE_MARK	ZB036

DRYDOCK	DRYDOCK	BB090

FENCE/WALL	FENCE	AL070

FENDER	FENDER	BB198

FERRY_ROUTE	FERRY_CROSSING	AQ070

MARINE_FARM	FISH_HATCHERY	BH050

FISHING_FACILITY	FISHING_FACILITY	BD079

FISHING_HARBOR	FISHING_HARBOR	BB105

PROMENADE_PIER	FISHING_PIER	AK190

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	FACC	FACC CODE	FACC ATTRIBUTE/VALUE

FLOATING_DOCK	FLOATING_DOCK	BB199

FOG_SIGNAL	FOG_SIGNAL	BC101

FORTIFIED_STRUCTURE	FORTIFICATION	AH050

FOUL_GROUND	FOUL_GROUND	BD050

GATE	GATE_(NAUTICAL)	BI041

GAUGING_STATION	GAUGING_STATION	BI070

GRAIN_ELEVATOR/ELEVATOR	GRAIN_ELEVATOR	AM030

GRIDIRON	GRIDIRON	BB115

SHORELINE_CONSTRUCTION	Groin	GROIN	BB043

HARBOR	HARBOR	BB005

MOORED_VESSEL	HULK	BD181

ICE_BOOM	ICE_BOOM	BB202

ISLAND	ISLAND	BA030

ISOGONIC_LINE	ISOGONIC_LINE	ZC050

MAGNETIC_VARIATION	ISOGONIC_LINE	ZC050

NAMED_WATER_AREA	Lagoon/Reef Pool	LAGOON	BH190

LAKE	LAKE	BH080

VEGETATION	LAND_USE/LAND_COVER	EB030

LANDING_PLACE	LANDING_PLACE	BB150

LEADING_LINE	LEADING_LINE	BC100

LIGHT_VESSEL/LIGHTSHIP	LIGHT	BC040

NAVIGATION_LIGHT	LIGHT	BC040

LOCK	LOCK	BI030

LOG_POND	LOG_BOOM	BD071

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	FACC	FACC CODE	FACC ATTRIBUTE/VALUE

MAGNETIC_DISTURBANCE_AREA	MAGNETIC_DISTURBANCE_AREA	ZC040

PRECAUTIONARY_AREA	MARITIME_AREA	FC031	MAC - 42 Precautionary Area

OFFSHORE_PRODUCTION_AREA	MARITIME_AREA	FC031	MAC - 98 Offshore Production

FREEPORT_AREA	MARITIME_AREA	FC031	MAC - 79 Free Port Area

CUSTOM_ZONE	MARITIME_AREA	FC031	MAC - 1 Customs Area

UNSURVEYED_AREA	MARITIME_AREA	FC031	MAC - 26 Unsurveyed Area

PILOT_BOARDING_PLACE	MARITIME_AREA	FC031	MAC - 48 Pilot Boarding Area

CAUTION_AREA	MARITIME_AREA	FC031	MAC - 42 Precautionary Area

WILDLIFE_MANAGEMENT_AREA	Marine Sanctuary	MARITIME_AREA	FC031	MAC - 80 Fish Sanctuary

MILITARY_PRACTICE_AREA	MARITIME_AREA	FC031	MAC - 91Practice Area in

INSHORE_TRAFFIC_ZONE	MARITIME_AREA	FC031	MAC - 41 Inshore Traffic Zone

DUMPING_GROUND	MARITIME_AREA	FC031	MAC - 30 Dumping Ground for

INCINERATION_AREA	MARITIME_AREA	FC031	MAC - 31 Incineration Area

TERRITORIAL_SEA_AREA	MARITIME_AREA	FC031	MBL - Territorial Waters - Limits

CARGO_TRANSHIPMENT_AREA	MARITIME_AREA	FC031	MAC - 49 Cargo Transshippment

TERRITORIAL_SEA_AREA	MARITIME_AREA	FC031	MBL - Limits of Sovereignty

CONTINENTAL_SHELF_AREA	MARITIME_LIMIT_BOUNDARY	FC021	MBL - 10 Continental Shelf

STRAIGHT_TERRITORIAL_BASELINE	MARITIME_LIMIT_BOUNDARY	FC021	MBL - 7 Territorial Waters

FISHERY_ZONE	MARITIME_LIMIT_BOUNDARY	FC021	MBL - 3 Fishing Zone Boundary

CONTIGUOUS_ZONE	MARITIME_LIMIT_BOUNDARY	FC021	MBL - 12 Limit of Contiguous

COAST_GUARD_STATION	MARITIME_STATION/MARITIME_SIGNAL	BB155	STA - 1 Coast Guard

VISUAL_SIGNAL_STATION	MARITIME_STATION/MARITIME_SIGNAL	BB155	STA - 34 Signal Station, Traffic

SWAMP/MARSH	MARSH/SWAMP	BH095

MEASURED_DISTANCE_LINE	MEASURED_DISTANCE_LINE	FC100

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	FACC	FACC CODE	FACC ATTRIBUTE/VALUE

MINE-NAVAL	MINE-NAVAL	BD001

SHORELINE_CONSTRUCTION	Mole	MOLE	BB042

MOORING_FACILITY	MOORING/WARPING_FACILITY	BB079

DOLPHIN	MOORING/WARPING_FACILITY	BB079

MOORING_FACILITY	Mooring Ring	MOORING_RING	BB160

NAVIGATION_LINE	NAVIGATION_LINE	BC031

OBSTRUCTION	OBSTRUCTION_(NAUTICAL)	BD070

OFFSHORE_LOADING_FACILITY	OFFSHORE_LOADING_FACILITY	BB170

OFFSHORE_PLATFORM	OFFSHORE_PLATFORM_SITE_(CLEARED	BD111

OIL_BARRIER	OIL_BARRIER	BD073

PARK	PARK	AK120

PARKING_AREA	PARKING_AREA	AQ140

PIER/WHARF/QUAY	PIER	BB190

PILE/POST	PILING	BD100

OFFSHORE_PLATFORM	PLATFORM	BD110

PONTOON	PONTOON	BD072

HARBOR_FACILITY	PORT_FACILITY	SU003

PORT_AUTHORITY	PORT_FACILITY	SU003

HARBOR_FACILITY	PORT_FACILITY	SU003

OVERHEAD_PIPELINE/CABLE	POWER_TRANSMISSION_LINE	AT030

LANDMARK	Tower	POWER_TRANSMISSION_PYLON	AT040

RADAR_RANGE	RADAR RANGE	BC033

RADAR_LINE	RADAR_LINE	BC032

RADAR_STATION	RADAR_TRANSMITTER	AT045

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	FACC	FACC CODE	FACC ATTRIBUTE/VALUE

RAILROAD	RAILROAD	AN010

RAILROAD_YARD	RAILROAD_YARD	AN060

BOAT_RAMP	RAMP_(MARITIME)	BB220

RAPIDS	RAPIDS	BH120

REEF	REEF	BD120

RESTRICTED_AREA	RESTRICTED_AREA	FC036	MAC - 7 Restricted Area

RIVER_BANK	RIVER_BANK	BH141

ROAD	ROAD	AP030

TWO_WAY_ROUTE	ROUTE_(MARITIME)	FC165	RTT - 11Two-way Route

SAFETY_FAIRWAY	ROUTE_(MARITIME)	FC165	RTT - 8 Safety Fairway/Channel

DEEP_WATER_ROUTE	ROUTE_(MARITIME)	FC165	RTT - 98 Deep Water Route

RECOMMENDED_TRACK	ROUTE_(MARITIME)	FC165

RUNWAY	RUNWAY	GB055

SANDBAR	SAND_LINE	BE022

SEA-PLANE_LANDING_AREA	SEA-PLANE_LANDING_AREA	GB070

SEA-PLANE_LANDING_AREA	SEAPLANE_BASE	GB065

SEAWALL	SEAWALL	BB230

SHORELINE_CONSTRUCTION	Stone Bank Paving	SHORELINE_CONSTRUCTION	BB081

SHORELINE_CONSTRUCTION	ACM Revetment Composite	SHORELINE_CONSTRUCTION	BB081

SLIPWAY	SLIPWAY/PATENT_SLIP	BB240

SMALL_CRAFT_FACILITY	SMALL_CRAFT_FACILITY	BB201

SOUNDING	SOUNDING	BE020

ELEVATION	SPOT_ELEVATION	CA030

SPRING	SPRING	BH170	HYC

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	FACC	FACC CODE	FACC ATTRIBUTE/VALUE

DREDGED_AREA	SWEPT_AREA	FC177	MAC  2 - Dredged Area

SWEPT_AREA	SWEPT_AREA	FC177

SILO/TANK	TANK	AM070	PRO

SUBMERGED_PIPELINE/CABLE	Telephone Cable	TELEPHONE_LINE	AT060

PYLON	TELEPHONE_POLE	AT070

TIDE_DATA_POINT	TIDE_DATA_POINT	BG030

TIDEWAY	TIDEWAY	BG011

TRAFFIC_SEPARATION_SCHEME	TRAFFIC_SEPARATION_SCHEME	FC041

TUNNEL	TUNNEL	AQ130

WATER_TOWER	WATER_TOWER	AM080

WATER_TURBULENCE	WATER_TURBULENCE	BG012

RIVER	WATERCOURSE	BH140

WATERFALL	WATERFALL	BH180

LANDMARK	Windmill/Motor	WINDMILL	AJ050

WRECK	WRECK	BD180

APPENDIX B2 - STANDARD CORRELATION OF FACC (Attribute Cross Reference) (INFORMATIVE)

ADMINISTRATION_AREA	HS001

ACC	Accuracy Category	HORIZ_ACC

NA2	Second name	COMMON_NAME

NA4	Country Code	COUNTRY

NAM	Name	FORMAL_NAME

USE	Usage	CATEGORY

BEACON	HS006

ACC	Accuracy Category	VERT_ACC

CCC	Color Code Category	PRIMARY_COLOR

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

NAM	Name	FORMAL_NAME

PAT	Buoy/Beacon Pattern Category	COLOR_PATTERN

SHP	Shape of Beacon	SHAPE

TMC	Top Mark Characteristic	CARDINAL

ZV2	Highest Z-Value	ELEVATION

BERTH	HS007

BER	Berth Identifier	DESIGNATOR

BOAT_RAMP	HS009

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

VRR	Vertical Reference Category	VERT_ACC

WID	Width	WIDTH

BOTTOM_CHARACTERISTICS	HS010

MCS	Material Composition Secondary	MATERIAL

MCU	Material Composition Underlying	NATURE_BOTTOM

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

BRIDGE	HS012

AAH	Absolute Horizontal Accuracy	HORIZ_ACC

AAV	Absolute Vertical Accuracy	VERT_ACC

BSC	Bridge /Bridge Superstructure Category	BRIDGE_TYPE

EXS	Existence Category	CONDITION

IDN	Identification Number	DESIGNATOR

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	CONSTRUCTION

MVC	Maximum Vertical Clearance	MATERIAL

NAM	Name	FORMAL_NAME

NOS	Number of Spans	NUM_SPANS

OHB	Overall Height of Bridge	HEIGHT

SHC	Safe Horizontal Clearance	HORIZ_CLEARAN

TXT	Text Attribute	DESCRIPTION

VCS	Vertical Clearance, Safe	VERT_CLEARANC

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

BRIDGE_PIER	HS013

ACC	Accuracy Category	VERT_ACC

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	VERT_LENGTH

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

BRIDGE_TOWER	HS014

AAH	Absolute Horizontal Accuracy	HORIZ_ACC

AAV	Absolute Vertical Accuracy	VERT_ACC

EXS	Existence Category	CONDITION

LEN	Length/Diameter	VERT_LENGTH

NAM	Name	FORMAL_NAME

OHB	Overall Height of Bridge	HEIGHT

SMC	Surface Material Category	CONSTRUCTION

UID	Unique Identifier	DESIGNATOR

WID	Width	WIDTH

BUILDING	HS015

AAV	Absolute Vertical Accuracy	VERT_ACC

ACC	Accuracy Category	HORIZ_ACC

BFC	Building Function Category	FUNCTION

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

UID	Unique Identifier	DESIGNATOR

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

BUILT-UP_AREA	HS016

ACC	Accuracy Category	VERT_ACC

BAC	Built-Up Area Classification	FACC_CAT

EXS	Existence Category	CONDITION

MCC	Material Composition Category	MATERIAL

NAM	Name	FORMAL_NAME

PHT	Predominant Height	HEIGHT

WID	Width	WIDTH

BUOY	HS017

BTC	Beacon/Buoy Type Category	FACC_CAT

CCC	Color Code Category	PRIMARY_COLOR

COL	Character of Light	CHARACTER

NAM	Name	FORMAL_NAME

PAT	Buoy/Beacon Pattern Category	COLOR_PATTERN

PER	Period of Light	PERIOD

REF	Radar Reflector Attribute	RADAR_REFLECT

SSC	Structure Shape Category	SHAPE

TMC	Top Mark Characteristic	TOP_MARK

TXT	Text Attribute	DESCRIPTION

CANAL	HS018

ACC	Accuracy Category	HORIZ_ACC

EXS	Existence Category	CONDITION

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

PRC	Periodic Restriction Category	RESTRICTION

WDA	Water Depth Average	DEPTH

WID	Width	WIDTH

WV1	Water Velocity Average 1	WATER_VELOCIT

CARGO_TRANSHIPMENT_AREA	HS019

NAM	Name	FORMAL_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

CAUSEWAY	HS020

HGT	Height Above Surface Level	CLEARANCE

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

PFH	Predominant Feature Height	HEIGHT

SMC	Surface Material Category	CONSTRUCTION

WID	Width	WIDTH

CAUTION_AREA	HS021

NAM	Name	COMMON_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

COAST_GUARD_STATION	HS025

NAM	Name	FORMAL_NAME

CONTIGUOUS_ZONE	HS026

NA4	Country Code	COUNTRY

NAM	Name	COMMON_NAME

CONTINENTAL_SHELF_AREA	HS027

NA4	Country Code	COUNTRY

NAM	Name	FORMAL_NAME

CONVEYOR	HS029

AAV	Absolute Vertical Accuracy	VERT_ACC

ACC	Accuracy Category	HORIZ_ACC

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

UID	Unique Identifier	DESIGNATOR

WID	Width	WIDTH

CRANE	HS030

AAV	Absolute Vertical Accuracy	VERT_ACC

ACC	Accuracy Category	HORIZ_ACC

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	MATERIAL

SSC	Structure Shape Category	SHAPE

TXT	Text Attribute	DESCRIPTION

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

CUSTOM_ZONE	HS032

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

DAM	HS033

AVA	Absolute Vertical Accuracy in Meters	VERT_ACC

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

DEEP_WATER_ROUTE	HS035

HDI	Hydrographic Depth /Height Information	DEPTH_ACC

NAM	Name	FORMAL_NAME

DREDGED_AREA	HS040

NAM	Name	FORMAL_NAME

DRYDOCK	HS041

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

DUMPING_GROUND	HS042

NAM	Name	FORMAL_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

ELEVATION	HS044

AAV	Absolute Vertical Accuracy	VERT_ACC

ACC	Accuracy Category	HORIZ_ACC

MCC	Material Composition Category	MATERIAL

UID	Unique Identifier	DESIGNATOR

ZV2	Highest Z-Value	ELEVATION

FENCE/WALL	HS046

FTI	Fence Type Indicator	S_57_CAT

OHD	Obstacle Height/Depth Category	HEIGHT

WID	Width	WIDTH

FERRY_ROUTE	HS048

FCL	Ferry Crossing Length	TRIP_LENGTH

FER	Ferry Type	S_57_CAT

FISHERY_ZONE	HS049

NA4	Country Code	COUNTRY

NAM	Name	FORMAL_NAME

FISHING_HARBOR	HS052

NAM	Name	FORMAL_NAME

FOG_SIGNAL	HS057

SST	Sound Signal Type	S_57_CAT

TXT	Text Attribute	DESCRIPTION

FORTIFIED_STRUCTURE	HS058

ACC	Accuracy Category	VERT_ACC

AHA	Absolute Horizontal Accuracy in Meters	HORIZ_ACC

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

FOUL_GROUND	HS059

ACC	Accuracy Category	VERT_ACC

HDI	Hydrographic Depth /Height Information	HEIGHT

HDP	Hydrographic Depth	DEPTH

FREEPORT_AREA	HS060

NAM	Name	FORMAL_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

GATE	HS061

GNC	Gate (Nautical) Classification	S_57_CAT

MCC	Material Composition Category	CONSTRUCTION

WID	Width	WIDTH

GAUGING_STATION	HS062

NAM	Name	FORMAL_NAME

GRAIN_ELEVATOR/ELEVATOR	HS063

ACC	Accuracy Category	HORIZ_ACC

AVA	Absolute Vertical Accuracy in Meters	VERT_ACC

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

SSC	Structure Shape Category	SHAPE

TXT	Text Attribute	DESCRIPTION

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

GRIDIRON	HS064

NAM	Name	FORMAL_NAME

HARBOR	HS066

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

ICE_AREA	HS068

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

INCINERATION_AREA	HS070

HDP	Hydrographic Depth	DEPTH

NAM	Name	FORMAL_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

INSHORE_TRAFFIC_ZONE	HS071

HDP	Hydrographic Depth	DEPTH

MAC	Maritime Area Category	FACC_CAT

NAM	Name	COMMON_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

ISLAND	HS072

HGT	Height Above Surface Level	HEIGHT

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

LAKE	HS074

NAM	Name	FORMAL_NAME

SCC	Spring/Well Characteristic Category	FACC_CAT

WID	Width	WIDTH

LANDING_PLACE	HS075

WID	Width	WIDTH

LANDMARK	HS076

AAV	Absolute Vertical Accuracy	VERT_ACC

ACC	Accuracy Category	HORIZ_ACC

DIR	Directivity	Directivity

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

HOD	Horizontal Datum Classification	HORIZ_DATUM

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

SSC	Structure Shape Category	SHAPE

TXT	Text Attribute	DESCRIPTION

UID	Unique Identifier	DESIGNATOR

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

LIGHT_VESSEL/LIGHTSHIP	HS079

AHA	Absolute Horizontal Accuracy in Meters	HORIZ_ACC

AVA	Absolute Vertical Accuracy in Meters	VERT_ACC

CCC	Color Code Category	PRIMARY_COLOR

COL	Character of Light	CHARACTER

HGT	Height Above Surface Level	HEIGHT

HOD	Horizontal Datum Classification	HORIZ_DATUM

LVN	Light Range, Nominal	RANGE

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

PAT	Buoy/Beacon Pattern Category	COLOR_PATTERN

PER	Period of Light	PERIOD

TXT	Text Attribute	DESCRIPTION

VDC	Vertical Datum Category	VERT_DATUM

LOCK	HS080

ACC	Accuracy Category	HORIZ_ACC

DIR	Directivity	DIRECTIVITY

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	MATERIAL

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

LOG_POND	HS082

LEN	Length/Diameter	LENGTH

WID	Width	WIDTH

MAGNETIC_DISTURBANCE_AREA	HS083

TXT	Text Attribute	DESCRIPTION

VAV	Variation Anomaly Value	MAG_ANOMALY

MAGNETIC_VARIATION	HS084

MAG	Magnetic Variation	VARIATION

TXT	Text Attribute	DESCRIPTION

MARINE_FARM	HS086

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

MEASURED_DISTANCE_LINE	HS088

LOR	Length of Range	LENGTH

NAM	Name	FORMAL_NAME

MILITARY_PRACTICE_AREA	HS089

NAM	Name	FORMAL_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

MINE-NAVAL	HS090

ACC	Accuracy Category	HORIZ_ACC

HDP	Hydrographic Depth	DEPTH

MID	Mine Identity Classification	IDENTIFIER

MSC	Mine Status Classification	STATUS

MTN	Mine Track Number	DESIGNATOR

NAMED_WATER_AREA	HS093

NAM	Name	FORMAL_NAME

NAVIGATION_LIGHT	HS094

AHA	Absolute Horizontal Accuracy in Meters	HORIZ_ACC

AOO	Angle of Orientation	ORIENTATION

AVA	Absolute Vertical Accuracy in Meters	VERT_ACC

CCC	Color Code Category	PRIMARY_COLOR

HGT	Height Above Surface Level	HEIGHT

HLT	Hydrographic Light Type	CATEGORY

HOD	Horizontal Datum Classification	HORIZ_DATUM

LVN	Light Range, Nominal	RANGE

MCA	Morse Code Attribute	SIG_GROUP

MCC	Material Composition Category	MATERIAL

NAM	Name	FORMAL_NAME

PAT	Buoy/Beacon Pattern Category	COLOR_PATTERN

PER	Period of Light	SIG_PERIOD

TXT	Text Attribute	DESCRIPTION

VDC	Vertical Datum Category	VERT_DATUM

ZV2	Highest Z-Value	ELEVATION

OFFSHORE_LOADING_FACILITY	HS097

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	VERT_LENGTH

NAM	Name	FORMAL_NAME

SMC	Surface Material Category	CONSTRUCTION

SSC	Structure Shape Category	SHAPE

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

OFFSHORE_PLATFORM	HS098

AHA	Absolute Horizontal Accuracy in Meters	HORIZ_ACC

AVA	Absolute Vertical Accuracy in Meters	VERT_ACC

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

OPC	Offshore Platform Classification	S_57_CAT

TXT	Text Attribute	DESCRIPTION

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

OFFSHORE_PRODUCTION_AREA	HS099

EXS	Existence Category	CONDITION

HDP	Hydrographic Depth	DEPTH

NAM	Name	FORMAL_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

OVERHEAD_PIPELINE/CABLE	HS101

AAV	Absolute Vertical Accuracy	VERT_ACC

AHA	Absolute Horizontal Accuracy in Meters	HORIZ_ACC

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	MATERIAL

TXT	Text Attribute	DESCRIPTION

UID	Unique Identifier	DESIGNATOR

VCS	Vertical Clearance, Safe	VERT_CLEARANC

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

PARK	HS102

NAM	Name	COMMON_NAME

PARKING_AREA	HS103

LEN	Length/Diameter	LENGTH

WID	Width	WIDTH

PIER/WHARF/QUAY	HS104

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

NAM	Name	FORMAL_NAME

SMC	Surface Material Category	CONSTRUCTION

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

PILE/POST	HS105

ACC	Accuracy Category	VERT_ACC

HGT	Height Above Surface Level	HEIGHT

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

PILOT_BOARDING_PLACE	HS106

HDP	Hydrographic Depth	DEPTH

NAM	Name	FORMAL_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

PRECAUTIONARY_AREA	HS109

HDP	Hydrographic Depth	DEPTH

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

PRODUCTION_AREA	HS110

AAV	Absolute Vertical Accuracy	VERT_ACC

ACC	Accuracy Category	HORIZ_ACC

BFC	Building Function Category	FUNCTION

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

HOD	Horizontal Datum Classification	HORIZ_DATUM

MCC	Material Composition Category	MATERIAL

NAM	Name	FORMAL_NAME

PRO	Product Category	PRODUCT

TXT	Text Attribute	DESCRIPTION

UID	Unique Identifier	DESIGNATOR

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

PROMENADE_PIER	HS111

HGT	Height Above Surface Level	HEIGHT

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

PYLON	HS112

AHA	Absolute Horizontal Accuracy in Meters	HORIZ_ACC

AVA	Absolute Vertical Accuracy in Meters	VERT_ACC

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

HOD	Horizontal Datum Classification	HORIZ_DATUM

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

RADAR_STATION	HS116

ACC	Accuracy Category	VERT_ACC

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

RADAR_TRANSPONDER_BEACON	HS117

ACC	Accuracy Category	HORIZ_ACC

CCC	Color Code Category	PRIMARY_COLOR

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

ZV2	Highest Z-Value	ELEVATION

RADIO_CALLING_IN_POINT	HS118

NAM	Name	FORMAL_NAME

RADIO_STATION	HS119

ACC	Accuracy Category	HORIZ_ACC

AOO	Angle of Orientation	ORIENTATION

AVA	Absolute Vertical Accuracy in Meters	VERT_ACC

BRF	Broadcast Frequency	COMM_CHANNEL

HOD	Horizontal Datum Classification	HORIZ_DATUM

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	MATERIAL

FEATURE NAME

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

UID	Unique Identifier	DESIGNATOR

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

RAILROAD	HS120

ACC	Accuracy Category	VERT_ACC

EXS	Existence Category	CONDITION

NAM	Name	FORMAL_NAME

RAILROAD_YARD	HS121

CTL	Cumulative Track Length	TRACK_LENGTH

NAM	Name	COMMON_NAME

WID	Width	WIDTH

RAPIDS	HS122

LEN	Length/Diameter	HEIGHT

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

RECOMMENDED_TRACK	HS123

HDP	Hydrographic Depth	DEPTH

NAM	Name	FORMAL_NAME

REEF	HS124

ACC	Accuracy Category	HORIZ_ACC

HDP	Hydrographic Depth	DEPTH

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	MATERIAL

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

RESCUE_STATION	HS125

AAV	Absolute Vertical Accuracy	VERT_ACC

ACC	Accuracy Category	HORIZ_ACC

BFC	Building Function Category	FUNCTION

HGT	Height Above Surface Level	HEIGHT

IDN	Identification Number	IDENTIFIER

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	MATERIAL

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

UID	Unique Identifier	DESIGNATOR

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

RESTRICTED_AREA	HS126

TXT	Text Attribute	DESCRIPTION

RIVER	HS128

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

WDA	Water Depth Average	DEPTH

WID	Width	WIDTH

ROAD	HS131

ACC	Accuracy Category	HORIZ_ACC

EXS	Existence Category	CONDITION

MED	Median Category	MATERIAL

NAM	Name	FORMAL_NAME

RST	Road/Runway Surface Type	SURFACE

RTN	Route Number	DESIGNATOR

SMC	Surface Material Category	CONSTRUCTION

WID	Width	WIDTH

RUNWAY	HS132

ACC	Accuracy Category	HORIZ_ACC

EXS	Existence Category	CONDITION

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

RST	Road/Runway Surface Type	SURFACE

SMC	Surface Material Category	CONSTRUCTION

UID	Unique Identifier	DESIGNATOR

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

SAFETY_FAIRWAY	HS133

HDI	Hydrographic Depth /Height Information	VERT_DATUM

HDP	Hydrographic Depth	DEPTH

NAM	Name	FORMAL_NAME

SEA-PLANE_LANDING_AREA	HS136

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

ZV3	Airfield/Aerodrome elevation	ELEVATION

SHORELINE	HS138

ACC	Accuracy Category	VERT_ACC

SHO	Shoreline Category	FACC_CAT

SLT	Shoreline Type Category	S_57_CAT

TXT	Text Attribute	DESCRIPTION

VDC	Vertical Datum Category	VERT_DATUM

SHORELINE_CONSTRUCTION	HS139

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

SMC	Surface Material Category	CONSTRUCTION

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

SILO/TANK	HS140

AAH	Absolute Horizontal Accuracy	HORIZ_ACC

AAV	Absolute Vertical Accuracy	VERT_ACC

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

HOD	Horizontal Datum Classification	HORIZ_DATUM

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

PRO	Product Category	PRODUCT

SSC	Structure Shape Category	SHAPE

TXT	Text Attribute	DESCRIPTION

UID	Unique Identifier	DESIGNATOR

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

SLIPWAY	HS141

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

SOUNDING	HS144

ACC	Accuracy Category	HORIZ_ACC

HDP	Hydrographic Depth	DEPTH

NAM	Name	FORMAL_NAME

SPRING	HS145

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

STRAIGHT_TERRITORIAL_BASELINE	HS146

NA4	Country Code	COUNTRY

NAM	Name	COMMON_NAME

SUBMERGED_PIPELINE/CABLE	HS148

AAV	Absolute Vertical Accuracy	VERT_ACC

AHA	Absolute Horizontal Accuracy in Meters	HORIZ_ACC

EXS	Existence Category	CONDITION

HOD	Horizontal Datum Classification	HORIZ_DATUM

LEN	Length/Diameter	HEIGHT

MCC	Material Composition Category	MATERIAL

TXT	Text Attribute	DESCRIPTION

UID	Unique Identifier	DESIGNATOR

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

SWAMP/MARSH	HS149

NAM	Name	FORMAL_NAME

SWEPT_AREA	HS150

HDP	Hydrographic Depth	DEPTH

TERRITORIAL_SEA_AREA	HS151

NAM	Name	COMMON_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

TIDAL_STREAM	HS152

CRN	Current Rate Minimum	MIN_RATE

CRX	Current Rate Maximum	MAX_RATE

CUR	Current Type Category	S_57_CAT

NAM	Name	FORMAL_NAME

TXT	Text Attribute	DESCRIPTION

TIDE_DATA_POINT	HS153

NAM	Name	FORMAL_NAME

TRAFFIC_SEPARATION_SCHEME	HS156

IAS	IMO Adoption Status	STATUS

TUNNEL	HS157

EXS	Existence Category	CONDITION

HCA	Horizontal Clearance Attribute	HORIZ_CLEARAN

LEN	Length/Diameter	LENGTH

MVC	Maximum Vertical Clearance	VERT_CLEARANC

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

TWO_WAY_ROUTE	HS159

HDP	Hydrographic Depth	DEPTH

NAM	Name	COMMON_NAME

UNSURVEYED_AREA	HS161

NAM	Name	COMMON_NAME

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

VEGETATION	HS162

NAM	Name	FORMAL_NAME

VEG	Vegetation Characteristics	S_57_CAT

VISUAL_SIGNAL_STATION	HS163

NAM	Name	FORMAL_NAME

STA	Station Type Category (Maritime)	S_57_CAT

WATER_TOWER	HS165

AAH	Absolute Horizontal Accuracy	HORIZ_ACC

AAV	Absolute Vertical Accuracy	VERT_ACC

EXS	Existence Category	CONDITION

HGT	Height Above Surface Level	HEIGHT

HOD	Horizontal Datum Classification	HORIZ_DATUM

LEN	Length/Diameter	LENGTH

MCC	Material Composition Category	CONSTRUCTION

NAM	Name	FORMAL_NAME

SSC	Structure Shape Category	SHAPE

TXT	Text Attribute	DESCRIPTION

UID	Unique Identifier	DESIGNATOR

VDC	Vertical Datum Category	VERT_DATUM

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

WATER_TURBULENCE	HS166

NAM	Name	FORMAL_NAME

WATERFALL	HS167

DIR	Directivity	Directivity

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

WID	Width	WIDTH

ZV2	Highest Z-Value	ELEVATION

WILDLIFE_MANAGEMENT_AREA	HS168

HDP	Hydrographic Depth	DEPTH

NAM	Name	FORMAL_NAME

OPS	Operational Status	STATUS

TXT	Text Attribute	DESCRIPTION

WID	Width	WIDTH

WRECK	HS169

ACC	Accuracy Category	HORIZ_ACC

HDP	Hydrographic Depth	DEPTH

HGT	Height Above Surface Level	HEIGHT

LEN	Length/Diameter	LENGTH

NAM	Name	FORMAL_NAME

TNG	Tonnage	TONNAGE

TXT	Text Attribute	DESCRIPTION

WDT	Date of Report	DATE_START

WID	Width	WIDTH

WK1	Wreck Type	S_57_CAT

ZV2	Highest Z-Value	ELEVATION

APPENDIX C1 - STANDARD CORRELATION OF REEGIS (Feature Cross Reference) (INFORMATIVE)

HYDRO STANDARD FEATURE	    HYDRO ATTRIBUTE/VALUE	             REEGIS		REEGIS ATTRIBUTE/VALUE

ADMINISTRATION_AREA	City	CITY

ADMINISTRATION_AREA	County	COUNTY

ADMINISTRATION_AREA	State	STATE

ADMINISTRATION_AREA	Coast Guard District	COAST GUARD DISTRICT

ADMINISTRATION_AREA	COE District	CORPS DISTRICT

AIRPORT/AIRFIELD	AIRFIELD

ANCHORAGE_AREA	ANCHORAGE AREA

BEACON	NAVIGATION MARKER	marker_type

BOAT_RAMP	BOAT RAMP

BREAKWATER	JETTY

BRIDGE	BRIDGE

BRIDGE_PIER	BRIDGE PIER

BUILDING	STRUCTURE	layer Building

BUILDING	STRUCTURE	layer Warehouse

BUILDING	STRUCTURE	layer Dwelling

BUILDING	STRUCTURE	layer Factory

BUOY	NAVIGATION BUOY

CANAL	CANAL

CHANNEL_RIVER_SYSTEM(SHALLOW)	Access	ACCESS CHANNEL

CHANNEL_RIVER_SYSTEM(SHALLOW)	Alignment	CHANNEL ALIGNMENT

CONTROL_POINT	HORIZONTAL CONTROL POINT

HYDRO STANDARD FEATURE	    HYDRO ATTRIBUTE/VALUE	             REEGIS		REEGIS ATTRIBUTE/VALUE

CURRENT	DIRECTION OF FLOW

DAM	DAM AREA

DAY_MARK	NAVIGATION MARKER	marker_type  Passing

DEPTH_CONTOUR	DEPTH CONTOURS

DISTANCE_MARK	RIVER MILE

DOLPHIN	DOLPHIN

DREDGED_AREA	DREDGED AREA

DUMPING_GROUND	DISPOSAL AREA

DYKE	DIKE

FENDER	FENDER SYSTEM

FERRY_ROUTE	FERRY CROSSING

FLEETING_AREA	FLEETING AREA

FLOOD_DIVERSION_AREA	FLOODWAY

FLOODWALL	FLOODWALL

GAUGING_STATION	GAGING STATION

GRAIN_ELEVATOR/ELEVATOR	ELEVATOR

GUIDE_WALL	LOCK GUIDE WALL

HARBOR	HARBOR

HARBOR_FACILITY	PORT

ISLAND	ISLAND

LAKE	LAKE

LANDMARK	Tower	UTILITY TOWER

HYDRO STANDARD FEATURE	    HYDRO ATTRIBUTE/VALUE	             REEGIS		REEGIS ATTRIBUTE/VALUE

LEVEE	FRONTLINE LEVEE

LOCK	LOCK

LOCK_BASIN/LOCK_CHAMBER	LOCK CHAMBER

MAJOR_INFLOW/OUTFLOW_STRUCTURE	MAJOR INFLOW/OUTFLOW STRUCTURE

MAT_CASTING_FIELD	MAT CASTING FIELD

MOORED_VESSEL	GAMING BOAT

NAMED_WATER_AREA	Crossing	CROSSING

NAMED_WATER_AREA	Chute	CHUTE

NAMED_WATER_AREA	Bend	BEND

NAVIGATION_LIGHT	NAVIGATION LIGHT

OBSTRUCTION	NAV HAZARD

OFFSHORE_PLATFORM	PLATFORM

OVERHEAD_PIPELINE/CABLE	TRANSMISSION LINE

PARK	PARK

PARKING_AREA	PARKING AREA

PORT_AUTHORITY	PORT AUTHORITY

PRECAUTIONARY_AREA	SAFETY ZONE

PRODUCTION_AREA	REFINERY

RAILROAD	RAILROAD SINGLE

RAILROAD_YARD	RAILROAD YARD

RECOMMENDED_TRACK	SAILING LINE

RIVER	PERENNIAL RIVER/PERENNIAL STREAM

HYDRO STANDARD FEATURE	    HYDRO ATTRIBUTE/VALUE	             REEGIS		REEGIS ATTRIBUTE/VALUE

RIVER_BANK	RIVER EDGE

RIVER_ENGINEERING_STRUCTURE	Dike System	DIKE SYSTEM

RIVER_ENGINEERING_STRUCTURE	Bendway Weir	BENDWAY WEIR

RUNWAY	RUNWAY

SAFETY_FAIRWAY	FAIRWAY

SANDBAR	SANDBAR

SHORELINE	WATER EDGE

SHORELINE_CONSTRUCTION	Slope Paving	LEVEE SLOPE PAVING

SHORELINE_CONSTRUCTION	ACM Revetment	ACM REVETMENT COMPOSITE

SHORELINE_CONSTRUCTION	Stone Bank Paving	STONE BANK PAVING

SILO/TANK	STRUCTURE	layer Tank

SILO/TANK	TANK

SMALL_CRAFT_FACILITY	MARINA

SOUNDING	SOUNDINGS

SUBMERGED_PIPELINE/CABLE	Pipeline	PIPELINE

SUBMERGED_PIPELINE/CABLE	TV Cable	CABLE TV LINE

SUBMERGED_PIPELINE/CABLE	Telephone Cable	PHONE LINE

SWAMP/MARSH	SWAMP

TRAFFIC_SEPARATION_SCHEME	SAFETY ZONE

TUNNEL	TUNNEL

TURNING_BASIN	TURNING BASIN

VEGETATION	LAND COVER

HYDRO STANDARD FEATURE	    HYDRO ATTRIBUTE/VALUE	             REEGIS		REEGIS ATTRIBUTE/VALUE

WILDLIFE_MANAGEMENT_AREA	Federal	FEDERAL WILDLIFE MANAGEMENT AREA.

WILDLIFE_MANAGEMENT_AREA	State	STATE WILDLIFE MANAGEMENT AREA

WRECK	WRECK SUNKEN/EXPOSED

APPENDIX C2 - STANDARD CORRELATION OF REEGIS (Attribute Cross Reference) (INFORMATIVE)

ADMINISTRATION_AREA	HS001

Pname	FORMAL_NAME

Ptype	CATEGORY

AIRPORT/AIRFIELD	HS002

Afname	FORMAL_NAME

ANCHORAGE_AREA	HS004

anname	FORMAL_NAME

permit id	PERMIT

BEACON	HS006

marker type	SPECIAL_PURPOSE

BOAT_LIFT	HS008

Wlabel	COMMON_NAME

BOAT_RAMP	HS009

Bdate	DATE_START

Bname	FORMAL_NAME

BRIDGE	HS012

bname	FORMAL_NAME

Bridge Drawing	DESCRIPTION

Bstatus	STATUS

btype	BRIDGE_TYPE

Road Elev	ELEVATION

vertical clearance	VERT_CLEARANCE

BRIDGE_PIER	HS013

Bname	FORMAL_NAME

BUILDING	HS015

Material Type	CONSTRUCTION

No of Floors	NO_FLOORS

Slab Elevation	ELEVATION

Sname	FORMAL_NAME

BUOY	HS017

Bname	FORMAL_NAME

Buoy Type	FACC_CAT

Flash Sequence	CHARACTER

CHECKPOINT	HS024

Project Depth	DEPTH

CONTROL_POINT	HS028

datum	VERT_DATUM

Elevation	ELEVATION

hdate	DATE_START

hdescription	DESCRIPTION

hname	FORMAL_NAME

DAM	HS033

Base Width	WIDTH

Cdate	DATE_START

Dname	FORMAL_NAME

Record Drawing	DESCRIPTION

Spillway Length	LENGTH

DAY_MARK	HS034

S_57_CAT

mname	FORMAL_NAME

DEPTH_AREA	HS036

year	RECORD_DATE

DEPTH_CONTOUR	HS037

Vdatum	VERT_DATUM

Water Surface Elevation	DEPTH

DISTANCE_MARK	HS038

River Mile	RIVER_MILE

Year	SOURCE_DATE

DOLPHIN	HS039

Dname	FORMAL_NAME

DREDGED_AREA	HS040

Cut Length	LENGTH

Permit No	PERMIT

Reach Name	FORMAL_NAME

Start Date	SOURCE_DATE

DUMPING_GROUND	HS042

dname	FORMAL_NAME

start date	SOURCE_DATE

DYKE	HS043

Dlength	LENGTH

Dname	COMMON_NAME

Weir Elevation	ELEVATION

FENDER	HS047

Flength	LENGTH

Fname	FORMAL_NAME

Width	WIDTH

FERRY_ROUTE	HS048

Fname	FORMAL_NAME

FLEETING_AREA	HS053

Fname	COMMON_NAME

Permit Number	PERMIT

Remarks	DESCRIPTION

FLOOD_DIVERSION_AREA	HS055

Fname	COMMON_NAME

Remarks	DESCRIPTION

FLOODWALL	HS056

Date Constructed	DATE_START

Elevation	ELEVATION

Fname	FORMAL_NAME

Height	HEIGHT

Record Drawing	DESCRIPTION

FOUL_GROUND	HS059

hname	FORMAL_NAME

htype	S_57_CAT

FEATURE NAME

GAUGING_STATION	HS062

Gage notes	DESCRIPTION

Gname	FORMAL_NAME

GRAIN_ELEVATOR/ELEVATOR	HS063

Material Type	CONSTRUCTION

Slab Elevation	ELEVATION

Sname	FORMAL_NAME

GUIDE_WALL	HS065

Lgname	FORMAL_NAME

Wall Length	LENGTH

HARBOR	HS066

Hname	COMMON_NAME

Project Depth	DEPTH

HARBOR_FACILITY	HS067

Port Name	FORMAL_NAME

ICE_BOOM	HS069

hname	FORMAL_NAME

htype	S_57_CAT

remarks	DESCRIPTION

ISLAND	HS072

Gname	FORMAL_NAME

Year	SOURCE_DATE

LAKE	HS074

Gname	FORMAL_NAME

Year	SOURCE_DATE

LEVEE	HS078

Levee Name	COMMON_NAME

LOCK_BASIN/LOCK_CHAMBER	HS081

Llength	LENGTH

Lname	FORMAL_NAME

Width	WIDTH

MOORED_VESSEL	HS091

Gname	FORMAL_NAME

Permit No	PERMIT

NAMED_WATER_AREA	HS093

Rlname	FORMAL_NAME

NAVIGATION_LIGHT	HS094

Nname	COMMON_NAME

OBSTRUCTION	HS096

Hname	FORMAL_NAME

Htype	S_57_CAT

Remarks	DESCRIPTION

OFFSHORE_PLATFORM	HS098

Material Type	CONSTRUCTION

Slab elevation	ELEVATION

Sname	FORMAL_NAME

OVERHEAD_PIPELINE/CABLE	HS101

Uname	COMMON_NAME

Vertical Clearance	VERT_CLEARANCE

PARK	HS102

Pname	COMMON_NAME

PARKING_AREA	HS103

Parking Spaces	SPACES

Pname	FORMAL_NAME

PORT_AUTHORITY	HS108

Pname	FORMAL_NAME

PRECAUTIONARY_AREA	HS109

Remarks	DESCRIPTION

Zname	FORMAL_NAME

PRODUCTION_AREA	HS110

Material Type	MATERIAL

Slab Eevation	ELEVATION

Sname	FORMAL_NAME

RAILROAD	HS120

Rname	FORMAL_NAME

RAILROAD_YARD	HS121

Rname	COMMON_NAME

RIVER	HS128

Sname	FORMAL_NAME

RIVER_BANK	HS129

Condition	CONDITION

RIVER_ENGINEERING_STRUCTURE	HS130

Blength	LENGTH

name	FORMAL_NAME

Original Condition	CONDITION

Remarks	DESCRIPTION

ROAD	HS131

Rname	FORMAL_NAME

RUNWAY	HS132

Afname	FORMAL_NAME

SAFETY_FAIRWAY	HS133

Fname	FORMAL_NAME

Remarks	DESCRIPTION

SANDBAR	HS135

Gname	FORMAL_NAME

Year	RECORD_DATE

SHORELINE_CONSTRUCTION	HS139

Original Condition	CONDITION

Record Drawing	DESCRIPTION

Rname	FORMAL_NAME

Stone Finish Date	DATE_END

Stone Start Date	DATE_START

Stone Type	CONSTRUCTION

Top Elevation	ELEVATION

SILO/TANK	HS140

Material Type	CONSTRUCTION

Slab Elevation	ELEVATION

Sname	FORMAL_NAME

SMALL_CRAFT_FACILITY	HS143

Cdate	SOURCE_DATE

Mname	FORMAL_NAME

SOUNDING	HS144

Vdatum	VERT_DATUM

SUBMERGED_PIPELINE/CABLE	HS148

Date Constructed	SOURCE_DATE

Diameter	DIAMETER

Pname	COMMON_NAME

Transport Mat	PRODUCT

Uname	FORMAL_NAME

TRAFFIC_SEPARATION_SCHEME	HS156

Remarks	DESCRIPTION

Zname	FORMAL_NAME

TURNING_BASIN	HS158

Cdate	SOURCE_DATE

Record Drawing	DESCRIPTION

Tlength	LENGTH

Tname	FORMAL_NAME

Twidth	WIDTH

WILDLIFE_MANAGEMENT_AREA	HS168

Mname	FORMAL_NAME

WRECK	HS169

Remarks	DESCRIPTION

Wname	FORMAL_NAME

Wtype	S_57_CAT

APPENDIX D1 - STANDARD CORRELATION OF TSSDS (Feature Cross Reference) (INFORMATIVE)

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	TSSDS	TSSDS ATTRIBUTE/VALUE

ADMINISTRATION_AREA	COE District	DISTRICT AREA	dis_typ_d    COE

ADMINISTRATION_AREA	Coast Guard District	DISTRICT AREA	dis_typ_d    COAST_GUARD

ADMINISTRATION_AREA	State	POLITICAL JURISDICTION AREA	govern_d     STATE

ADMINISTRATION_AREA	County	POLITICAL JURISDICTION AREA	govern_d     COUNTY

ADMINISTRATION_AREA	City	POLITICAL JURISDICTION AREA	govern_d     MUNICIPALITY

AIRPORT/AIRFIELD	AIRFIELD

ANCHOR_BERTH	ANCHOR BERTH

ANCHORAGE_AREA	RESTRICTED ANCHORAGE AREA

AQUATIC_VEGETATION_AREA	AQUATIC VEGETATION AREA

BEACON	MARINE NAVIGATION BEACON

BERTH	BERTH

BOAT_RAMP	BOAT RAMP

BREAKWATER	JETTY

BRIDGE	ROAD BRIDGE AREA

BRIDGE_PIER	PYLON/PIER SUPPORT

BUILDING	PERMANENT STRUCTURE

BUOY	BUOY

CANAL	CANAL

CAUSEWAY	CAUSEWAY

CAUTION_AREA	CAUTION AREA

CHECKPOINT	CHECKPOINT

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	TSSDS	TSSDS ATTRIBUTE/VALUE

COAST_GUARD_STATION	COAST GUARD STATION

CONTROL_POINT	CONTROL POINT

CONVEYOR	CONVEYOR

CRANE	CRANE

CURRENT	FLOW DIRECTION ARROW

DAM	DAM

DEEP_WATER_ROUTE	DEEP WATER ROUTE

DEPTH_CONTOUR	DEPTH CONTOUR

DISTANCE_MARK	DISTANCE MARKER

DOLPHIN	DOLPHIN

DREDGED_AREA	DREDGED AREA

DRYDOCK	DRYDOCK

DUMPING_GROUND	DREDGED BANK

DYKE	DIKE

ELEVATION	SPOT ELEVATION	spot_typ_d  GROUND

FENCE/WALL	FENCE

FENDER	MARINE FENDER

FERRY_ROUTE	FERRY CROSSING

FISHING_GROUND	FISHING SITE

FLEETING_AREA	FLEETING SITE

FLOATING_DOCK	FLOATING DRYDOCK

FLOOD_DIVERSION_AREA	FLOODWAY

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	TSSDS	TSSDS ATTRIBUTE/VALUE

FLOODWALL	FLOODWALL

GAUGING_STATION	GAUGING STATION

GRAIN_ELEVATOR/ELEVATOR	GRAIN ELEVATOR

GUIDE_WALL	LOCK GUIDE WALL

HARBOR	HARBOR

ICE_AREA	ICE

ISLAND	ISLAND

LAKE	SURFACE WATER BODY	perman_d PERMANENT

LANDING_PLACE	LANDING SITE

LANDMARK	Smokestack/Chimney	SMOKESTACK/CHIMNEY POINT

LEADING_LINE	NAVIGATION RANGE LINE

LEVEE	LEVEE

LIGHT_VESSEL/LIGHTSHIP	NAVIGATION LIGHT

LOCK	LOCK

LOCK_BASIN/LOCK_CHAMBER	LOCK CHAMBER

LOG_POND	LOG POND

MAJOR_INFLOW/OUTFLOW_STRUCTURE	STORM SEWER HEADWALL POINT

MARINE_FARM	WATER FARM

MAT_CASTING_FIELD	CASTING FIELD

MOORED_VESSEL	MOORED VESSEL

NAMED_WATER_AREA	NAMED RIVER FEATURE

NAVIGATION_LINE	NAVIGATION RANGE LINE

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	TSSDS	TSSDS ATTRIBUTE/VALUE

OBSTRUCTION	NAVIGATION OBSTRUCTION SITE	obstyp_d  (All Other)

OVERHEAD_PIPELINE/CABLE	Electrical Cable	ELECTRICAL CABLE	instl_ty_d SERVICE_OH

OVERHEAD_PIPELINE/CABLE	Electrical Cable	ELECTRICAL CABLE	instl_ty_d PRIMARY_OH

OVERHEAD_PIPELINE/CABLE	Electrical Cable	ELECTRICAL CABLE	instl_ty_d SECONDARY_OH

PARK	RECREATION PARK

PARKING_AREA	PARKING LOT

PIER/WHARF/QUAY	MOORING FACILITY

PILOT_BOARDING_PLACE	PILOT BOARDING SITE

PONTOON	FLOATING PONTOON

PORT_AUTHORITY	DISTRICT AREA	dis_typ_d  PORT AUTHORITY

PYLON	UTILITY POLE TOWER	design_d    POLE

RADIO_CALLING_IN_POINT	CALLING IN POINT

RAILROAD	RAILROAD CENTERLINE

RAILROAD_YARD	RAILROAD YARD

RAPIDS	RAPIDS

RECOMMENDED_TRACK	RECOMMENDED ROUTE LINE

REEF	NAVIGATION OBSTRUCTION SITE	obstyp_d  REEF

RESTRICTED_AREA	MARINE RESTRICTION AREA

RIVER	SURFACE WATER COURSE	perman_d PERMANENT

RIVER_BANK	RIVER BANK LINE

RIVER_ENGINEERING_STRUCTURE	Bendway Weir	BENDWAY WEIR SYSTEM

ROAD	ROAD

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	TSSDS	TSSDS ATTRIBUTE/VALUE

RUNWAY	AIRFIELD SURFACE	sur_use_d    RUNWAY

SAND_WAVES	SHOAL

SANDBAR	SANDBAR

SEA-PLANE_LANDING_AREA	SEA PLANE LANDING AREA

SHORELINE	SHORELINE

SHORELINE_CONSTRUCTION	Stone Bank Paving	STONE BANK PAVING AREA

SMALL_CRAFT_FACILITY	SMALL CRAFT MARINA

SOUNDING	SOUNDING

SPRING	SPRING

STRAIGHT_TERRITORIAL_BASELINE	STRAIGHT TERRITORIAL BASELINE

SUBMARINE_TRANSIT_LANE	SUBMARINE ROUTE

SUBMERGED_PIPELINE/CABLE	TV Cable	CABLE TELEVISION LINE	cab_elev_d

SUBMERGED_PIPELINE/CABLE	TV Cable	CABLE TELEVISION LINE	cab_elev_d

SWEPT_AREA	DEPTH MAINTENANCE AREA	clrmth_d SWEPT

TRAFFIC_SEPARATION_SCHEME	TRAFFIC SEPARATION SCHEME

TUNNEL	TUNNEL

TURNING_BASIN	TURNING BASIN

UNDERWATER_ROCK	UNDERWATER ROCK

UNSURVEYED_AREA	UNSURVEYED AREA

VEGETATION	LAND VEGETATION AREA

WAITING_AREA/LOCK_ARRIVAL_POINT	LOCK ARRIVAL POINT

WATER_TOWER	WATER TANK

HYDRO STANDARD FEATURE	HYDRO ATTRIBUTE/VALUE	TSSDS	TSSDS ATTRIBUTE/VALUE

WATER_TURBULENCE	WATER TURBULENCE

WATERFALL	WATERFALL

WRECK	WRECK

APPENDIX D2 - STANDARD CORRELATION OF TSSDS (Attribute Cross Reference)

ADMINISTRATION_AREA	HS001

bdjurpol	dist_desc	DESCRIPTION

bdjurpol	dist_name	FORMAL_NAME

bdjurpol	govern_d	CATEGORY

bdjurpol	polit_name	COMMON_NAME

AIRPORT/AIRFIELD	HS002

traflafd	active_d	STATUS

traflafd	feat_name	FORMAL_NAME

ANCHOR_BERTH	HS003

trmaranc	feat_name	FORMAL_NAME

ANCHORAGE_AREA	HS004

trmaracg	feat_name	FORMAL_NAME

trmaracg	permit_no	PERMIT

trmaracg	restrictn	RESTRICTION

AQUATIC_VEGETATION_AREA	HS005

flhabaqv	date_surv	SOURCE_DATE

flhabaqv	feat_name	FORMAL_NAME

flhabaqv	veg_desc	DESCRIPTION

BEACON	HS006

trnavbec	beac_con_d	CONSTRUCTION

trnavbec	color_d	PRIMARY_COLOR

trnavbec	feat_name	FORMAL_NAME

BERTH	HS007

trhrbber	feat_name	FORMAL_NAME

BOAT_LIFT	HS008

flhabaqv	date_surv	SOURCE_DATE

flhabaqv	feat_name	FORMAL_NAME

flhabaqv	veg_desc	DESCRIPTION

trnavwrk	wrk_label	COMMON_NAME

BOAT_RAMP	HS009

imrecbtr	date_end	DATE_END

imrecbtr	feat_desc	DESCRIPTION

imrecbtr	feat_name	FORMAL_NAME

BREAKWATER	HS011

trhrbjet	feat_name	FORMAL_NAME

BRIDGE	HS012

trvehbrg	brdg_ht	HEIGHT

trvehbrg	brdg_len	LENGTH

trvehbrg	brdg_stt_d	STATUS

trvehbrg	brdg_typ_d	BRIDGE_TYPE

trvehbrg	brg_draw	DESCRIPTION

trvehbrg	brg_mat_d	CONSTRUCTION

trvehbrg	brg_width	WIDTH

trvehbrg	color_d	PRIMARY_COLOR

trvehbrg	date_dedic	DATE_START

trvehbrg	feat_name	FORMAL_NAME

trvehbrg	road_elev	ELEVATION

trvehbrg	struct_num	DESIGNATOR

trvehbrg	vert_clr	VERT_CLEARANC

BRIDGE_PIER	HS013

trgenpyl	feat_name	FORMAL_NAME

BUILDING	HS015

bggenstr	narrative	DESCRIPTION

bggenstr	str_cnd_d	CONDITION

bggenstr	structhght	HEIGHT

bggenstr	structname	FORMAL_NAME

BUOY	HS017

trnavboy	buoy_typ_d	FACC_CAT

trnavboy	color_d	PRIMARY_COLOR

trnavboy	feat_name	FORMAL_NAME

trnavboy	flash_seq	CHARACTER

trnavboy	narrative	DESCRIPTION

trnavboy	shape_d	SHAPE

CANAL	HS018

hysurcrs	crs_desc	DESCRIPTION

hysurcrs	crs_name	FORMAL_NAME

hysurcrs	length	LENGTH

hysurcrs	perman_d	STATUS

hysurcrs	veloc_mean	WATER_VELOCIT

CAUTION_AREA	HS021

trmarcau	feat_name	COMMON_NAME

trmarcau	narrative	DESCRIPTION

CHANNEL_MAINTAINED(DEEP_DRAF	HS023

trmarchn	date_end	DATE_END

trmarchn	date_srv	SOURCE_DATE

trmarchn	dep_dat_d	VERT_DATUM

trmarchn	feat_name	FORMAL_NAME

COAST_GUARD_STATION	HS025

trgenchk	narrative	DESCRIPTION

trnavcgs	feat_name	FORMAL_NAME

CONTROL_POINT	HS028

gdsrvmnt	adj_elev	ELEVATION

gdsrvmnt	date_estab	DATE_START

gdsrvmnt	date_recov	SOURCE_DATE

gdsrvmnt	feat_name	FORMAL_NAME

gdsrvmnt	narrative	DESCRIPTION

gdsrvmnt	vert_acc_d	VERT_ACC

gdsrvmnt	vert_dat_d	VERT_DATUM

CONVEYOR	HS029

immaccon	feat_desc	DESCRIPTION

immaccon	feat_len	LENGTH

immaccon	feat_name	FORMAL_NAME

immaccon	width	WIDTH

CRANE	HS030

immaccrn	feat_name	FORMAL_NAME

FEATURE NAME

immaccrn	height	HEIGHT

DAM	HS033

imfdcdam	base_width	WIDTH

imfdcdam	dam_typ_d	CONSTRUCTION

imfdcdam	date_built	DATE_START

imfdcdam	end_date	DATE_END

imfdcdam	feat_name	FORMAL_NAME

imfdcdam	rec_draw	DESCRIPTION

imfdcdam	splw_lgth	LENGTH

DEEP_WATER_ROUTE	HS035

trmarrte	dep_dat_d	VERT_DATUM

trmarrte	narrative	DESCRIPTION

DEPTH_CONTOUR	HS037

lfbthdep	area_desc	DESCRIPTION

lfbthdep	water_dep	DEPTH

DISTANCE_MARK	HS038

hysurdis	dis_ref	DESCRIPTION

hysurdis	year	SOURCE_DATE

DOLPHIN	HS039

trhrbdol	feat_name	FORMAL_NAME

DREDGED_AREA	HS040

imfdcspl	date_start	SOURCE_DATE

imfdcspl	feat_name	FORMAL_NAME

DRYDOCK	HS041

trhrbdry	feat_name	FORMAL_NAME

DUMPING_GROUND	HS042

imfdcspl	feat_name	FORMAL_NAME

DYKE	HS043

imfdcdik	date_start	SOURCE_DATE

imfdcdik	feat_name	COMMON_NAME

imfdcdik	length	LENGTH

imfdcdik	narrative	DESCRIPTION

imfdcdik	weir_elev	ELEVATION

ELEVATION	HS044

lfhypspt	elevation	ELEVATION

lfhypspt	feat_desc	DESCRIPTION

FENCE/WALL	HS046

imgenfnc	date_erect	SOURCE_DATE

imgenfnc	fenc_typ_d	CONSTRUCTION

imgenfnc	fence_ht	HEIGHT

FENDER	HS047

trhrbfen	date_inst	DATE_START

trhrbfen	feat_len	LENGTH

trhrbfen	feat_name	FORMAL_NAME

trhrbfen	width	WIDTH

FERRY_ROUTE	HS048

trmarrte	ferry_name	FORMAL_NAME

trmarrte	narrative	DESCRIPTION

FISHING_GROUND	HS051

imrecfsh	feat_desc	DESCRIPTION

imrecfsh	feat_name	FORMAL_NAME

FLEETING_AREA	HS053

trmarflt	feat_name	COMMON_NAME

trmarflt	narrative	DESCRIPTION

trmarflt	permit_no	PERMIT

FLOATING_DOCK	HS054

trhrbfld	feat_name	FORMAL_NAME

FLOOD_DIVERSION_AREA	HS055

imfdcfld	feat_name	COMMON_NAME

imfdcfld	narrative	DESCRIPTION

FLOODWALL	HS056

imfdcwal	date_built	DATE_END

imfdcwal	elevation	ELEVATION

imfdcwal	feat_name	FORMAL_NAME

imfdcwal	wall_ht	HEIGHT

GAUGING_STATION	HS062

imfdcgag	date_inst	DATE_START

imfdcgag	feat_name	FORMAL_NAME

imfdcgag	gage_desc	DESCRIPTION

GRAIN_ELEVATOR/ELEVATOR	HS063

immacgel	date_built	SOURCE_DATE

immacgel	feat_name	FORMAL_NAME

immacgel	max_ht	HEIGHT

immacgel	str_mat_d	CONSTRUCTION

GUIDE_WALL	HS065

trlocgwl	feat_len	LENGTH

trlocgwl	feat_name	FORMAL_NAME

HARBOR	HS066

trhrbare	feat_name	FORMAL_NAME

trhrbare	start_date	SOURCE_DATE

trhrbare	wat_depth	DEPTH

HARBOR_FACILITY	HS067

trhrbter	featname	FORMAL_NAME

trhrbter	narrative	DESCRIPTION

ICE_AREA	HS068

hyiceare	feat_desc	DESCRIPTION

hyiceare	feat_name	FORMAL_NAME

ISLAND	HS072

lftopisl	feat_desc	DESCRIPTION

lftopisl	feat_name	FORMAL_NAME

lftopisl	inhab_d	STATUS

LAKE	HS074

hysurwbd	body_desc	DESCRIPTION

hysurwbd	body_name	FORMAL_NAME

hysurwbd	body_typ_d	FACC_CAT

hysurwbd	year	SOURCE_DATE

LANDMARK	HS076

immacwnd	floor_elev	ELEVATION

immacwnd	narrative	DESCRIPTION

immacwnd	str_cnd_d	CONDITION

immacwnd	str_mat_d	CONSTRUCTION

immacwnd	str_stat_d	STATUS

immacwnd	str_use_d	FUNCTION

immacwnd	structhght	HEIGHT

immacwnd	structname	FORMAL_NAME

LEVEE	HS078

imeroacm	date_start	SOURCE_DATE

imeroacm	feat_name	COMMON_NAME

imeroacm	narrative	DESCRIPTION

LIGHT_VESSEL/LIGHTSHIP	HS079

trnavlit	flash_seq	PERIOD

trnavlit	lit_desig	FORMAL_NAME

LOCK	HS080

trlocsys	elev_delta	ELEVATION

trlocsys	lock_desig	FORMAL_NAME

LOCK_BASIN/LOCK_CHAMBER	HS081

trloccha	date_built	DATE_START

trloccha	feat_len	LENGTH

trloccha	lock_desig	FORMAL_NAME

trloccha	width	WIDTH

LOG_POND	HS082

hysurlog	feat_name	FORMAL_NAME

hysurlog	narrative	DESCRIPTION

MAJOR_INFLOW/OUTFLOW_STRUCT	HS085

utstohdw	feat_desc	DESCRIPTION

utstohdw	feat_name	FORMAL_NAME

MARINE_FARM	HS086

famgtffa	feat_desc	DESCRIPTION

famgtffa	feat_name	FORMAL_NAME

MOORED_VESSEL	HS091

trhrbves	feat_name	FORMAL_NAME

trhrbves	permit_no	PERMIT

MOORING_FACILITY	HS092

trhrbmft	feat_name	FORMAL_NAME

NAMED_WATER_AREA	HS093

hysurriv	feat_name	FORMAL_NAME

OBSTRUCTION	HS096

trnavobs	feat_name	FORMAL_NAME

trnavobs	narrative	DESCRIPTION

trnavobs	obstyp_d	S_57_CAT

OFFSHORE_PLATFORM	HS098

immacplt	date_start	DATE_START

immacplt	feat_name	FORMAL_NAME

immacplt	str_mat_d	CONSTRUCTION

OVERHEAD_PIPELINE/CABLE	HS101

utelecgp	cbl_length	LENGTH

utelecgp	cbl_mat_d	MATERIAL

utelecgp	cbl_typ_d	S_57_CAT

utelecgp	dispostn_d	STATUS

utelecgp	feat_desc	DESCRIPTION

utelecgp	feat_name	FORMAL_NAME

utelecgp	vert_clr	VERT_CLEARANC

PARK	HS102

imrecprk	feat_name	COMMON_NAME

PARKING_AREA	HS103

trvehprk	feat_desc	DESCRIPTION

trvehprk	feat_name	FORMAL_NAME

trvehprk	park_len	LENGTH

trvehprk	tot_spaces	SPACES

trvehprk	width	WIDTH

PIER/WHARF/QUAY	HS104

trhrbmor	feat_name	FORMAL_NAME

PILOT_BOARDING_PLACE	HS106

trmarplt	narrative	DESCRIPTION

PONTOON	HS107

trgenpon	narrative	DESCRIPTION

PORT_AUTHORITY	HS108

bdjurdst	dist_desc	DESCRIPTION

bdjurdst	dist_name	FORMAL_NAME

PRODUCTION_AREA	HS110

bggenstr	built_date	DATE_START

bggenstr	demol_date	DATE_END

bggenstr	floor_elev	ELEVATION

bggenstr	narrative	DESCRIPTION

bggenstr	str_cnd_d	CONDITION

bggenstr	str_mat_d	MATERIAL

bggenstr	str_stat_d	STATUS

bggenstr	structhght	HEIGHT

bggenstr	structname	FORMAL_NAME

PYLON	HS112

utgenpol	cond_d	CONDITION

utgenpol	date_acqrd	DATE_START

utgenpol	feat_name	FORMAL_NAME

utgenpol	mat_d	CONSTRUCTION

utgenpol	narrative	DESCRIPTION

utgenpol	poleheight	HEIGHT

utgenpol	type_d	S_57_CAT

RADIO_CALLING_IN_POINT	HS118

trmarcal	feat_name	FORMAL_NAME

trmarcal	narrative	DESCRIPTION

RAILROAD	HS120

trrrdrcl	feat_desc	DESCRIPTION

trrrdrcl	feat_name	FORMAL_NAME

trrrdrcl	line_stt_d	STATUS

trrrdrcl	rst_typ_d	CONDITION

RAILROAD_YARD	HS121

trrrdyrd	yard_name	COMMON_NAME

RAPIDS	HS122

hysurrap	feat_desc	DESCRIPTION

hysurrap	feat_leng	HEIGHT

hysurrap	feat_name	FORMAL_NAME

hysurrap	feat_width	WIDTH

RECOMMENDED_TRACK	HS123

trmarrte	dep_dat_d	VERT_DATUM

trmarrte	mean_depth	DEPTH

trmarrte	narrative	DESCRIPTION

REEF	HS124

trnavobs	feat_name	FORMAL_NAME

RESTRICTED_AREA	HS126

trmarres	restrction	RESTRICTION

RIVER	HS128

hysurcrs	crs_desc	DESCRIPTION

hysurcrs	feat_name	FORMAL_NAME

hysurcrs	length	LENGTH

hysurcrs	perman_d	STATUS

RIVER_BANK	HS129

gdsrvmnt	recov_cond	CONDITION

RIVER_ENGINEERING_STRUCTURE	HS130

imerobdw	date_built	DATE_START

imerobdw	feat_name	FORMAL_NAME

imerobdw	length	LENGTH

imerobdw	narrative	DESCRIPTION

imerobdw	ori_cond	CONDITION

ROAD	HS131

trvehrds	divided_d	MATERIAL

trvehrds	feat_desc	DESCRIPTION

trvehrds	feat_name	FORMAL_NAME

trvehrds	isur_seg_d	CONDITION

trvehrds	op_stat_d	STATUS

trvehrds	seg_typ_d	S_57_CAT

trvehrds	seg_width	WIDTH

trvehrds	srf_typ_d	CONSTRUCTION

RUNWAY	HS132

trairsur	air_cls_d	S_57_CAT

trairsur	feat_name	FORMAL_NAME

trairsur	feat_width	WIDTH

trairsur	run_stt_d	STATUS

trairsur	scope_code	DESCRIPTION

SAND_WAVES	HS134

lfbthshl	feat_desc	DESCRIPTION

SANDBAR	HS135

lfbthbar	area_desc	DESCRIPTION

lfbthbar	area_name	FORMAL_NAME

lfbthbar	vsmpl date	SOURCE_DATE

SEA-PLANE_LANDING_AREA	HS136

trairsea	feat_name	FORMAL_NAME

trairsea	restrictn	RESTRICTION

SHORELINE	HS138

hycznshr	bank_typ_d	FACC_CAT

hycznshr	shore_name	FORMAL_NAME

hycznshr	shr_typ_d	S_57_CAT

SHORELINE_CONSTRUCTION	HS139

imerostn	acm_length	LENGTH

imerostn	date_built	DATE_START

imerostn	date_end	DATE_END

imerostn	feat_name	FORMAL_NAME

imerostn	ori_cond	CONDITION

imerostn	rec_draw	DESCRIPTION

imerostn	revt_stt_d	STATUS

imerostn	stn_typ_d	CONSTRUCTION

imerostn	top_elev	ELEVATION

imerostn	vert_dat_d	VERT_DATUM

SILO/TANK	HS140

utgastnk	date_built	SOURCE_DATE

utgastnk	dispostn_d	STATUS

utgastnk	feat_name	FORMAL_NAME

utgastnk	max_ht	HEIGHT

utgastnk	model_no	DESIGNATOR

utgastnk	narrative	DESCRIPTION

utgastnk	str_mat_d	CONSTRUCTION

utgastnk	tank_legth	LENGTH

utgastnk	tank_st_d	S_57_CAT

utgastnk	tank_width	WIDTH

utgastnk	top_elv	ELEVATION

SMALL_CRAFT_FACILITY	HS143

imrecmar	date_built	SOURCE_DATE

imrecmar	feat_name	FORMAL_NAME

SOUNDING	HS144

lfbthdep	area_desc	DESCRIPTION

lfbthdep	water_dep	DEPTH

SPRING	HS145

hysurspr	feat_desc	DESCRIPTION

hysurspr	feat_name	FORMAL_NAME

STRAIGHT_TERRITORIAL_BASELINE	HS146

bdjurstb	authority	COUNTRY

bdjurstb	feat_name	COMMON_NAME

SUBMARINE_TRANSIT_LANE	HS147

trmarrte	narrative	DESCRIPTION

SUBMERGED_PIPELINE/CABLE	HS148

cotelcab	cbl_length	HEIGHT

cotelcab	cbl_mat_d	MATERIAL

cotelcab	cbl_typ_d	S_57_CAT

cotelcab	feat_desc	DESCRIPTION

cotelcab	feat_name	FORMAL_NAME

SWAMP/MARSH	HS149

hywetlnd	nwi_cls_d	S_57_CAT

hywetlnd	wetln_desc	DESCRIPTION

hywetlnd	wetln_name	FORMAL_NAME

SWEPT_AREA	HS150

lfbthsub	feat_desc	DESCRIPTION

lfbthsub	vert_dat_d	VERT_DATUM

TRAFFIC_SEPARATION_SCHEME	HS156

trmarsep	feat_name	FORMAL_NAME

trmarsep	narrative	DESCRIPTION

TUNNEL	HS157

trgentun	avg_wd	WIDTH

trgentun	feat_name	FORMAL_NAME

trgentun	length_tun	LENGTH

TURNING_BASIN	HS158

trhrbtrn	date_start	SOURCE_DATE

trhrbtrn	feat_name	FORMAL_NAME

trhrbtrn	length	LENGTH

trhrbtrn	rec_draw	DESCRIPTION

trhrbtrn	width	WIDTH

UNDERWATER_ROCK	HS160

lfbthudr	dep_dat_d	VERT_DATUM

UNSURVEYED_AREA			    HS161

lfbthuns	area_desc	DESCRIPTION

lfbthuns	date_desig	SOURCE_DATE

VEGETATION	HS162

flhabveg	date_sampl	SOURCE_DATE

flhabveg	feat_desc	DESCRIPTION

flhabveg	fgdc_cls_d	S_57_CAT

WATER_TOWER	HS165

utwattnk	date_aqrd	SOURCE_DATE

utwattnk	dispostn_d	CONDITION

utwattnk	narrative	DESCRIPTION

utwattnk	tank_lgth	LENGTH

utwattnk	tank_width	WIDTH

utwattnk	top_elv	ELEVATION

WATER_TURBULENCE	HS166

hysurtrb	cause	DESCRIPTION

hysurtrb	feat_name	FORMAL_NAME

WATERFALL	HS167

hysurwft	feat_desc	DESCRIPTION

hysurwft	feat_height	HEIGHT

hysurwft	feat_leng	LENGTH

hysurwft	feat_name	FORMAL_NAME

hysurwft	feat_width	WIDTH

WRECK	HS169

trnavwrk	narrative	DESCRIPTION

trnavwrk	ves_name	FORMAL_NAME

trnavwrk	wrck_typ_d	S_57_CAT

# Text boxes

Attribute Name

Attribute Code

Definition

Character Length

Data Type

Domain Name

Category Attribute

Value

Definition

Reference

Feature Type Name

Feature Code

Definitions

Object Type

Representation

Feature Name

Representation

Feature Code + “_FM”

Common Attributes specifying the physical characteristics of the feature; e.g. size, color, material, etc.

Feature Code + “_AT”

Unique Feature Attributes

Links to Related Tables

Feature Code + “_ID”

Common Attributes specifying the identifying characteristics of the feature; e.g. name, number, description, etc

Feature Code + “_ME”

Common Attributes specifying the metadata charactristics of feature data as identified in the FGDC Metadata Std